301 - Flight - Preflight, Performance Limits

Takeoff
Pitch trim (indicator on left cockpit wall):
  - If light and flaps up, nose down trim ... 1/2 unit
  - If heavy and flaps up, nose down trim ... 1 unit
  - If using flaps (15-25 deg) at any weight, nose down trim ... 1 1/2 unit
1. Rudder trim ... 1/2 unit STBD (right) (indicator on front canopy rim, right of gunsight)
2. Aileron trim ... Neutral (indicator on bottom center of instrument panel)
3. Prop RPM ... Max
4. Advancing right throttle slightly ahead of left can be useful to counter yaw on initial takeoff roll, or use differential brakes.
5. At 34 mph/30 kts, slight forward stick to raise the tail.
6. Rotate at approx 120 mph/104 kts??
7. Right stick might be required to counter a left roll tendency on takeoff.
8. When positively airborne, stop the wheels by hitting the brakes, then raise gear (Shift-T5 up to unlock gear handle and T5 up to raise gear).
9. Reduce boost to +9 and RPMs to 2850 (intermediate power, 1 hour limit) as soon as possible.
10. Best climb speed is 173 mph/150 kts.
11. Set supercharger to AUTO (Throttle Bottom Hat back to toggle), changeover happens at 15,000 ft.

Cruise
1. Cruise at +7 boost, weak mixture (Throttle Top Hat down, mixture lever goes up), and reduce RPM to minimum, or no more than 2650.
2. Max range speed is 196 mph/170 kts at any altitude. At lower altitudes you may not be able to go that slow, even with minimum RPM.
3. Keep supercharger in MOD position (switch down), unless you cannot maintain recommended speed under 2650 RPM, in which case switch supercharger to AUTO.

Landing
1. Check brake pressure ... 200 psi min
2. Supercharger switch ... MOD (switch down)
3. Radiators ... OPEN
4. Slow to 178 mph/155 kts and put down gear (check green lights)
5. Prop RPM ... Max
6. Flaps ... Full down (nose down trim will be needed)
7. Half fuel with no bombs approach speeds:
  - Engine-on: 125 mph/109 kts with flaps down, 140 mph/122 kts with flaps up
  - Engine-idle: 140 mph/122 kts with flaps down, 150 mph/130 kts with flaps up
  - At full load, increase speeds by 10 mph/9 kts.
1. After landing:
  1. Flaps up, lever neutral
  2. Pitot heat ... OFF