501 - A/G - Guns, Bombs, Rockets

Fence In
1. Gunsight power switch ... ON (right wall switches top row)
2. Gun Firing Master switch ... ON (B5 to open cover, B2 to turn on switch) (instrument panel center bottom, guarded switch)

Guns -- 4x .30 cal MG, 2x 20 mm cannon
Press Trigger S1 for MGs, Trigger S2 for MGs+cannons, or Flip-down Trigger for cannons only.

Bombs
On bomb control panel (lower center instrument panel, behind clear cover), set up bomb switches:
  - BUTTON CHANGE OVER switch ... ON (down) (barred double switch at the very top)
  - Top switch pair arms stations 1 and 2 (wing bombs).
  - Middle switch pair arms stations 3 and 4 (fuselage/bomb bay bombs).
  - Bottom switch pair sets nose and tail fuses.
When nearing target, open bomb bay doors (Gray Reset Hat back).
  - Doors take about 7 seconds to open.
1. Press Red Button to pickle selected bombs (armed stations).
2. Close bomb bay doors (Gray Reset Hat forward).

Rockets
1. Rockets Master Switch ... On (left wall just behind throttle quadrant)
2. Fire with Lower Gray Button (real trigger is on right throttle lever).
- Rockets fire in pairs, one pair per button press.
- If Rocket Salvo Mode switch is On (down) (dashboard left eyebrow panel), rockets will all fire simultaneously with one button press.