301 - Flight - Takeoff, Landing

Takeoff
1. Flaps ... Down one notch
2. Rotate around 70 kts.
3. Gear up before XXX??
4. Flaps up around 120 kts??
5. Best climb around 120 kts??

Landing
1. Engine Ignition Switch ... CONT IGN (aft position) (just in front of throttle)
2. Speedbrakes ... Out full, and keep out through landing
3. Under 200 kts: Landing gear ... Down
4. Under 190 kts: Flaps ... TAKE OFF (middle switch position)
5. Under 150 kts: Flaps ... DOWN FULL (bottom switch position)
6. Slow to On Speed AOA (approx 120 kts, top light=too slow, bottom light=too fast) and trim.
  - Will probably require full nose-up trim.
1. Adjust pitch with throttle.
2. Aim at end of runway. Approach angle/glideslope should be 3°.
3. Cut throttle at runway threshold, flare at 110 kts, touchdown at 95 kts, aerobrake until nose drops.
4. After stopping, retract airbrake, set flaps to up, and Engine Ignition Switch ... OFF (middle position).