303 - Flight - Navigation, ILS Landing

Navigation
     VOR TACAN VORTAC VOR-DME NDB NDB-DME
NDB with ADF receiver
1. On ADF panel (right console):
  1. Mode knob ... ADF
  2. Tune NDB frequency on one of the two readouts.
  3. Set TFR knob (between the two readouts) to point to left or right, whichever one you want to use.
2. Verify NAV button is lit (right-most of 3 buttons to left of HSI), which means it's using the receivers in your cockpit and not the other one.
3. Set HSI to ADF (button on right side of HSI, toggles ADF/NAV)
4. Set desired course to NDB on HSI (course knob on HSI panel on right console rear, or Middle Finger Hat up/down).
5. Thin white needle in RMI compass, and small dark red pointer in HSI compass, points to NDB beacon. HSI Course Deviation Indicator (displaced center of yellow line) on HSI doesn't work, but course can be lined up manually by flying to align the pointers.
VOR with VHF-NAV receiver
1. On VHF-NAV panel (right console):
  1. Mode knob ... NAV
  2. Tune VOR frequency on NAV frequency dials (right knob and readout)
2. Verify NAV button is lit (right-most of 3 buttons to left of HSI), which means it's using the receivers in your cockpit and not the other one.
3. Set HSI to NAV (button on right side of HSI, toggles ADF/NAV)
4. Set desired course to VOR on HSI (course knob on HSI panel on right console rear, or Middle Finger Hat up/down).
5. Double-line yellow needle in RMI compass, and small dark red pointer in HSI compass, points to VOR beacon. HSI also shows course deviation with displaced yellow line in the middle.
TACAN -- Uses TACAN for distance, VOR or ADF for bearing
C-101CC does not have a TACAN receiver, only C-101EB does. C-101CC can tune a TACAN freq (see built-in kneeboard pages for frequencies) on VOR receiver and get distance, but not bearing. To get bearing, tune a VOR or NDB station close to the TACAN.
1. Tune VHF-NAV NAV receiver as above to TACAN frequency (look up frequency for TACAN channel in built-in kneeboards), but set VHF-NAV Mode knob to DME (instead of NAV).
2. HSI will now show distance to TACAN station in top left readout.
3. Set desired course to VOR on HSI (course knob on HSI panel on right console rear, or Middle Finger Hat up/down).
4. Use a VOR near TACAN for bearing...:
  1. Set DME switch to HOLD (below HSI). This will keep the TACAN freq in use for DME while we re-tune for the VOR itself.
  2. Re-tune VHF-NAV NAV receiver as above to VOR frequency, with Mode knob still set to DME.
  3. HSI will now show bearing to VOR beacon with small dark red pointer.
5. ...or use an NDB near TACAN for bearing:
  1. Tune ADF receiver as above to NDB frequency.
  2. Set HSI to ADF (button on right side of HSI, toggles ADF/NAV)

ILS precision landing
See Takeoff/Landing kneeboard page.