501 - A/G - Guns, Unguided Bombs, Rockets

Fence In
1. Master Arm ... ON
2. Activate weapons stations

Guns -- 4x .30 cal MGs??
1. Gunsight ... 170 mils down
2. Fire with Trigger.

Rockets
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Weapon pylon buttons ... Select rocket pylons (top light on button turns yellow when selected)
  2. MODE knob ... ROC or BRST for single or ripple rockets respectively
    - 1-1 should be the correct setting for singles but doesn't work in the game. IRL, ROC would be used for a mixed launcher with both bombs and rockets.
1. Set gunsight depression (see tables on next page); 30 deg is a good default for steep dives or close range attacks (rocket motor still burning) (Middle Finger Hat up/down for tens, left/right for units)
2. Open stores release guard (Dish Hat up); stick grip will show safety guard up.
3. Fire with Red Button.

Rocket types
- Zuni
- 2.75" rockets

Bombs
1. On SCAR panel (bottom left instrument panel, above left knee):
  1. Weapon pylon buttons ... Select bomb pylons (top light on button turns yellow when selected)
  2. ARM knob ... NS/TL, NS, or TL as needed
  3. MODE knob ... As desired:
    1. BOMB ... If single pylon is selected, only that bomb will be dropped. If multiple pylons are selected, bombs will drop in pairs from inboard, outboard, center in that order with each pickle.
    2. RIP ... Selected pylons are rippled with timing set by RIPPLE TIME knob.
  4. RIPPLE TIME knob ... As desired if using RIP mode (time in milliseconds):
Speed	70 ms	90 ms	120 ms	150 ms	200 ms
200	24 ft	30 ft	41 ft	51 ft	68 ft
250	30 ft	38 ft	51 ft	63 ft	84 ft
300	35 ft	46 ft	61 ft	76 ft	101 ft
350	41 ft	53 ft	71 ft	89 ft	118 ft
400	47 ft	61 ft	81 ft	101 ft	135 ft
450	53 ft	68 ft	91 ft	114 ft	152 ft

1. Set gunsight depression (see tables on next page) (Middle Finger Hat up/down for tens, left/right for units)
2. Open stores release guard (Dish Hat up); stick grip will show safety guard up.
3. Fire with Red Button.

Bomb types
- 750 lb bomb
- Mk 82
- Mk 82 Snakeye
- Mk 83