201 - Cold Start

Cold Start -- WIP
1. Fuel selector valve ... MAIN
2. Rudder trim ... T.O. (Takeoff)
3. Aileron and Elevator trim ... Neutral
4. Turbo lever ... OFF
5. Throttle ... Full back
6. Mixture ... IDLE CUTOFF
8. GEN switch ... ON
9. Prop SELECTOR SWITCH ... AUTO CONSTANT SPEED
10. Cowl flaps ... Open
13. --------------------------------------
14. Main Fuel Selector Valve ... MAIN ON (left wall, floor) (shorter end of red handle points to selected item)
15. Oil and Intercooler shutters ... NEUTRAL (left wall)
16. Throttle ... 1 inch forward
17. Prop RPM lever ... Full forward
18. Prime engine:
  1. Primer handle is on top left instrument panel.
  2. Right-click to unlock.
  3. Left-click and hold to prime 4-6 times.
  4. Right-click to lock.
19. BATTERY switch ... ON
20. Ignition switch ... BOTH
21. STARTER switch ... ENGAGE (right-click) momentarily, then OFF (release click)
22. STARTER switch ... ENERGIZE (left-click and hold) for 15-20 seconds (until flywheel is spun up), then ENGAGE (right-click) and hold
23. After a few revs, Mixture lever ... AUTO RICH
24. Release STARTER switch
25. Set Throttle to 900 RPM
26. Monitor engine:
  1. Oil pressure must be 45-95 psi and steady (if it doesn't reach at least 25 psi during start, abort)
  2. Oil temperature must be at least 40 deg C
  3. SUCTION gauge must show 3.85-4.15 in. Hg (green zone)
27. Wait until engine oil pressure is at least 25 psi and temperature is at least 40 deg C.

Follow remaining steps in taxi and takeoff checklists on following page.