301 - Flight - Preflight, Takeoff, Landing, Jettison, Air Restart, Performance Limits

Taxi checklist
1. Unlock tail wheel, so you can S-turn to check visibility over the nose
2. Parking brake ... Off
3. Flaps retracted while taxiing.

Before takeoff checklist
1. If aux fuel tank is full, set elevator trim 1/4 inch forward of white mark.
2. Flaps ... Up
3. Gunsight ... On (TODO)
4. ....WIP

Takeoff
1. Brakes should hold full power.
2. Stick full aft at 95 to 100 kts.
3. Should lift off at 100 to 120 depending on load.
4. Gear up.
5. At 155 kts, flaps full up (hold switch until flaps are fully up, about 5 seconds).
6. Make sure gear and flaps are up before 190 kts (yellow line on airspeed indicator).
7. Best climb speed is 0.61 Mach at sea level to 0.8 Mach at 40,000 ft (according to real Sabre manual). Heavier load or higher air temperature means lower climb speed.
  - Best climb speed also implies the most excess thrust (difference between max thrust and thrust required to maintain level flight), therefore it's recommended to dogfight at speeds at or above best climb speed.

Landing
1. Deploy speed brakes and keep them out for the entire landing.
2. Slow down until airspeed is under 190 kts (yellow line on airspeed indicator).
3. Put down gear and full flaps.
4. Final approach speed about 145 kts.
5. Touchdown at 120 kts.
6. Retract flaps for maximum braking.

Jettison
Set fuel tank knob for tanks as needed (left console front).
  - If using both inboard and outboard tanks, outboard tanks should be emptied and dropped first.
1. Press red jettison button below tank selection knob to punch tanks.
2. Set fuel tank knob to ALL TANKS OFF.

Engine air start
1. Throttle ... OFF (pull throttle all the way back, press Shift-Bottom Thumb Button 2x to move throttle past idle detents to cutoff)
2. If possible, establish glide at 185 kts IAS.
3. Check engine RPM within restart limits of 23% to 34%. Up to 200 kts IAS may be required to windmill up to correct RPM.
4. Emergency Ignition switch ... ON
5. If main fuel system has failed: Emergency fuel switch ... ON
  - Don't use emergency fuel system if flameout was due to rapid throttle movement.
1. Throttle ... Idle (Bottom Thumb Button 2x) then advance slowly
2. At 90% RPM, Emergency Ignition switch ... OFF

Performance limits
- Fuel: 2826 lbs internal
  - with 2x 120 gal drop tanks (801 lbs ea.) = 4428 lbs
  - with 2x 200 gal drop tanks (1335 lbs ea.) = 5497 lbs
- "Maximum Continuous Thrust" is 87% to 96% RPM, "Military Thrust" is 100% RPM.
- Gear and flaps: below 190 kts (yellow line on airspeed indicator)
- With outer wing tanks: Below 25k ft, lower of 500 kts IAS or 0.90 Mach. No limit above 25k ft.
- Max EGT: 685 deg C