202 - Ground - Preflight, Performance Limits

General French stuff
M = Marche = ON/START
A = Arrêt = OFF/STOP
G = Gauche = LEFT
D = Droit = RIGHT
L = Lent = SLOW
R = Rapide = FAST

Before takeoff (hot start or auto started)
1. Artificial horizon mode knob ... DOP (upper instrument panel right side)
2. Flare Dispenser switch ... LE = slow or VE = fast (center console next to pilot's left thigh)??
3. Flare Dispenser quantity switch ... C/C = single or SEQ = sequence
4. Flare Dispenser cover ... Open (black and yellow striped cover on pilot's collective stick)
5. Radios ... On and tuned as needed (center lower instrument panel, press/click band button to make active radio)
6. Sand Filter ... ON if installed (switch above clock on pilot's lower instrument panel)
7. Arm weapons and activate TV sensor (see A/G weapons page)
8. Copilot laser and missile button covers ... Open (on copilot weapon grip)
9. Lights ... As desired (switches on upper center instrument panel under RWR, and ceiling)

Performance limits
- Main tank full is 83%, Aux tank is fuel above that amount??
- Max landing vertical speed: 60 m/min (a bit more than the first mark under 0 on the VSI)
- Engine limits: 8-12 seconds at or above 100% torque (red light on torque meter on solid)