201 - Ground - Cold Start

General French stuff
M = Marche = ON/START
A = Arrêt = OFF/STOP
G = Gauche = LEFT
D = Droit = RIGHT
L = Lent = SLOW
R = Rapide = FAST

Cold Start -- WIP
1. Cockpit doors ... Close (RCtrl-R)
2. Battery switch ... ON
3. Alternator switch ... ON
4. Generator switch ... ON
5. AM radio switch ... ON
6. NADIR mode ... VEILLE (initialize)
7. Fuel Pump switch ... ON
8. Wait 20 seconds for fuel pump to prime.
9. Starter switch ... ON
10. Wait for engine to reach idle (25,100 RPM) (25s).
11. Rotor Brake lever ... RELEASE (full forward) (large lever on ceiling)
12. Fuel Flow lever ... Slightly forward until rotor begins to rotate
  - Turbine RPM should be at about 29,000 for this.
1. When rotor RPM needle matches engine RPM needle: Fuel Flow lever ... Slowly forward all the way as engine and rotor spool up.
2. Pitot heat switch ... ON
3. Trim switch ... ON (enables trim hat)
4. Magnetic brake switch ... ON (enables stick centering trim)
5. Gyro Knob ... GM (begins gyro alignment, 60s)
6. Autopilot master switch ... ON
7. Autopilot pitch, roll, and yaw switches ... ON
8. Artificial horizon ... Uncage
9. Standby artificial horizon ... Uncage
10. Radar altimeter ... ON and set bug as desired

Proceed with pre-flight checks on next page.