202 - Ground - Preflight, Performance Limits

General French stuff
M = Marche = ON/START
A = Arrêt = OFF/STOP
G = Gauche = LEFT
D = Droit = RIGHT
L = Lent = SLOW
R = Rapide = FAST

Before takeoff (hot start or auto started)
1. Artificial horizon mode knob ... DOP (upper instrument panel right side)
2. Flare Dispenser switch ... LE = slow or VE = fast (center console next to pilot's left thigh)??
3. Flare Dispenser quantity switch ... C/C = single or SEQ = sequence
4. Flare Dispenser cover ... Open (black and yellow striped cover on pilot's collective stick)
5. Radios ... On and tuned as needed (center lower instrument panel, press/click band button to make active radio)
6. RWR ... ON (instrument panel top left, under RWR display)
7. Sand Filter ... ON if installed (switch above clock on pilot's lower instrument panel)
8. Arm weapons and activate TV sensor (see A/G weapons page)
9. Lights ... As desired (switches on upper center instrument panel under RWR, and ceiling)

Performance limits
- Max landing vertical speed: 60 m/min (a bit more than the first mark under 0 on the VSI)
- Engine limits: 8-12 seconds at or above 100% torque (red light on torque meter on solid)
- Max descent speed:
  - Over 30 kph (translational lift): Unlimited
  - Under 30 kph (no translational lift): ~4 m/s
- Max speed: ~300 kph (depends on air pressure, may be limited either due to retreating blade stall or to rotor coning in different conditions)
- When at or near max speed, avoid sudden maneuvers, particularly pitching up and to the right.