301 - Flight - NADIR navigation system

NADIR system general info
NADIR parameter knob (top knob):
Parameter	Top line	Bottom line
VENT	Wind direction (deg)	Wind speed (kph)
CM DEC	Magnetic heading (deg)	Magnetic declination (deg/min??)
VS DER	Doppler radar ground speed (kph)	Deviation (drift??) angle
TPS CAP	Heading to active waypoint (deg)	ETE to waypoint (minutes)
PP	Your current latitude (ddm*)	Your current longitude (ddm*)
BUT	Selected waypoint** latitude (ddm*)	Selected waypoint** longitude (ddm*)

* = In PP and BUT, switch between lat/long and UTM (note: not MGRS) with GEO UTM button on keypad.
** = Waypoint number is shown to left.
NADIR mode knob (bottom knob):
  - ARRET -- Off
  - VEILLE -- Standby/Alignment
  - TERRE -- Ground
  - MER -- Sea
  - ANEMO -- Anemometer (wind speed)
  - TEST SOL -- Ground test

Navigate to waypoint with NADIR
1. Mode knob ... TERRE
2. Parameter knob ... BUT
3. Press number on keypad to select waypoint (1-9).
  - Waypoint 1 is always your starting position??
HSI compass shows direction to waypoint with double-line needle, and distance in km in readout to above right.

Add/edit waypoint with NADIR
1. Mode knob ... TERRE
2. Parameter knob ... BUT
3. Press number 1-9 on keypad to select waypoint.
4. Press ENT to begin editing; top line will begin flashing.
  - Press Down Arrow button to toggle between top and bottom lines.
1. Press EFF (erase) repeatedly to clear flashing line.
2. For top line (latitude), press 2 for North or 8 for South, then enter latitude in DD MM.M format, then ENT.
3. Press Down Arrow button to go to bottom line.
4. Press EFF (erase) repeatedly to clear bottom line.
5. Press 4 for West or 6 for East, then enter longitude in DDD MM.M format, then ENT.

Store current location as a waypoint
1. Mode knob ... TERRE
2. Parameter knob ... PP
3. Press GEL button.
4. Parameter knob ... BUT
5. Press number 1-9 of waypoint you want to store location in, then ENT.