501 - A/G - All

Master Arm ... ON (B2 button, or switch on instrument panel under radar altimeter)
TV system ... ON

SA342M -- 4x HOT missiles
Viviene TV sighting system
Turn sighting system on (copilot seat, VCB = Video Command Box next to TV display):
1. VCB Power Selector knob ... M (ON) (VCB next to TV)
2. VCB IR Power Selector knob ... M (ON) (VCB next to TV)
3. VCB Mode Selector knob ... Pil for manual tracking, Ass to auto-follow moving targets (VCB next to TV)
4. TV On/Off switch ... ON (toggle switch under TV screen)
Prepare missiles (copilot seat):
1. Lasing button cover ... OPEN (copilot video stick)
2. Missile Launch button cover ... OPEN (copilot video stick)
3. Test On/Off key ... JOUR (day) or NUIT (night) as needed (instrument panel under TV and VCB)
4. HOT missile station selector knob ... as needed (Lower Gray Button to cycle) (instrument panel under TV and VCB)

HOT missiles
1. Prepare missiles and sighting system above
2. HOT missile station selector knob ... as needed (Lower Gray Button to cycle)
3. Lase target (TDC press) to establish range.
4. Max range is 4300 m.
5. Target is locked if white rectangle appears in lower right quadrant of TV crosshairs.
6. Come to a hover and press Speedbrake Hat up to engage autohover. Text appears in control indicator diagram when autohovering.
7. Must be within 3 degrees of centerline to fire missile. Press Pinky Button when autohovering to turn helicopter toward sight.
8. Press Red Button to fire.

SA342L -- 20 mm cannon with 240 rounds + 8x SNEB 68 mm rockets
Cannon
1. Gunsight glass ... Down (click to deploy)
2. Armament Panel Power switch ... M (ON) (center console forward)
3. Right Pylon Master Arm switch ... ARM (red guarded switch, center console) (if both are armed, only cannon will fire)
4. Press Trigger to fire.
SNEB rockets
1. Gunsight glass ... Down (click to deploy)
2. Armament Panel Power switch ... M (ON) (center console forward)
3. Left Pylon Master Arm switch ... ARM (red guarded switch, center console) (if both are armed, only cannon will fire)
4. Ripple/Single switch ... As desired (center console)
5. Press Trigger to fire.

SA342Minigun -- 7.62 mm Minigun
1. Minigun can only be fired by player.
2. Press 3 to go to gunner seat.
3. Aim with head tracking, fire with trigger.

SA342Mistral -- 4x Mistral IR A/A missiles
1. Gunsight glass ... Down (click to deploy)
2. Armament Panel Power switch ... M (ON) (center console forward)
3. Left and Right Pylon Master Arm switches ... ARM (red guarded switch, center console)
4. Ripple/Single switch ... As desired (center console)
5. Put target in reticle, get lock tone, press Trigger to fire.
  - You may have to be extremely close to get them to guide.