1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing, RWR, Navigation

Takeoff
1. Flaps ... Full down (Shift-T6 down, shows 2 lights in flaps indicator)
2. Begin takeoff run.
3. Rotate at 260 kph.
4. Put pitot tubes at the horizon for a good takeoff angle, about 13 degrees.
5. Raise gear immediately but build up speed before raising flaps. Raise flaps under 400 kph.

Landing
1. Under 400 kph, put down gear and flaps.
2. Pattern speed ~300 kph, final approach speed ~260 kph.
3. Landing speed ~220 to 240 kph.
4. Put pitot tubes at the horizon for a good takeoff angle, about 13 degrees.
5. Use drag chute if needed (Shift-T5 down)

RWR
- Light in outer ring of large circles indicates primary threat direction.
- Lights in small dots just inside those indicates secondary threats.
- Ring of dashed lines on the inside indicates range/signal strength of primary threat, weakest is all the way to the right, and getting stronger to the left. Ownship marker is the triangle at the left.
- Lights in bottom row of dashes and letters is primary (dashes) and secondary (letters) threat type:
  - П	З	X	H	F	C
  - AI radar	LR radar	MR radar	SR radar	EW radar	AWACS
- B and H lights in the center of the plane show relative elevation of primary threat. If both are lit, threat is co-altitude.
- Red flashing circle in the center around the plane is radar lock warning.
- Press Shift-E1 press to toggle RWR to filter out acquisition radars.

Navigation
- Press B5 to cycle NAV Master Modes: No Task, Route, Return, and Landing.
- Mode is indicated with lights on Navigation Panel by right knee:
  - No Task -- No lights.
  - En Route -- Navigates to regular pre-planned waypoints. First 3 lights on bottom row correspond to first 3 waypoints; waypoints over 3 have no lights.
  - Return -- Navigates to the runway approach point. One of the first 3 lights on the top row will be lit (1st light is takeoff airfield, 2nd is landing airfield, 3rd is any other airfield), and last light on bottom row will be lit.
  - Landing -- Navigates to the end of the actual runway. One of the first 3 lights on the top row will be lit (1st light is takeoff airfield, 2nd is landing airfield, 3rd is any other airfield), all others will be off.
- You're in No Task mode if there are two small red flags at the 10-and-2 o'clock positions on your artificial horizon.
- Distance to the next waypoint is shown next to the HSI.