051 - A/G - Stores List

Pods:
- L-081 Phantasmagoria	ELINT pod, required to use anti-radiation missiles
- Mercury LLTV pod	Low Light TV camera pod, provides night vision to Shkval TV
- MPS 410	ECM jammer (stations 1 and/or 8 only)

Guided weapons:
- Kh-25ML (AS-10 Karen)	Laser guided missile, 90 kg warhead, range 2-10 km
- Kh-25MP (AS-10 Karen)	Anti-radiation missile, (Hawk only?? not sure if any difference in game)
- Kh-25MPU (AS-10 Karen)	Anti-radiation missile, improved seeker (incl Roland?? not sure if any difference in game)
- Kh-29L (AS-14 Kedge)	Laser guided missile, 317 kg warhead, range 8-10 km
- Kh-29T (AS-14 Kedge)	TV guided missile, 317 kg warhead, range??
- Kh-58U (AS-11 Kilter)	Anti-radiation missile, 149 kg warhead, range 36-120 km depending on altitude
- S-25L	Laser guided rocket, 171 kg warhead, range 7 km
- 9A1472 Vikhr	Laser guided missile, range 8 km

Bombs:
- BetAB-500	Concrete piercing bomb, low-drag (no parachute or rocket)
- BetAB-500ShP	Concrete piercing bomb, high-drag (parachute and rocket)
  - Drop BetAB-500ShP between 150-1000 m
- FAB-100	GP HE bomb
- FAB-250	GP HE bomb
- FAB-500 M62	GP HE bomb
- KAB-500kr	TV guided bomb
- KMGU-2 - 96 AO-2.5RT	Submunition dispenser, frag
- KMGU-2 - 96 PTAB-2.5KO	Submunition dispenser, AP
  - Drop KMGUs between 50-150 m
- MDB-2-67U - 4 FAB-100	Multiple bomb rack with 4x FAB-100 GP HE bombs
- RBK-250 - PTAB-2.5M	Cluster bomb, AP
- RBK-250-275 - AO-1SCh	Cluster bomb, frag
- RBK-500 - PTAB-1M	Cluster bomb, AP
- RBK-500 - PTAB-10-5	Cluster bomb, AP
- RBK-500U - OAB-2.5RT	Cluster bomb, frag airbursting
  - Drop RBKs at 300 m minimum
- SAB-100	Illumination Bomb, drop between 1000-3000 m, Illumination lasts 1-5 minutes

Rockets:
- S-13 OF	122 mm, 5 rounds/pod, HE blast/frag warhead, 1.6-3.0 km range
- S-8OFP2	80 mm, 20 rounds/pod, 1.3-4.0 km range, HE blast/frag warhead
- S-8KOM	80 mm, 20 rounds/pod, 1.3-4.0 km range, HEAT warhead
- S-8TsM	80 mm, 20 rounds/pod, 1.3-4.0 km range, Smoke (often banned on servers due to lag issues)
- S-24B	240 mm, 123 kg blast/frag warhead, 2 km max range
- S-25 OFM	340 mm, 190 kg blast/frag warhead, 4 km max range
- S-5 KO	57 mm, 1.3 kg dual purpose HEAT/frag warhead, 3-4 km max range

Gun Pods:
SPPU-22-1 Gun Pod