402 - A/A - Guns, Missiles

Corner speed: 760

WVR combat and CAC (dogfight) modes
Use Dish Hat for CAC (dogfight) modes:
  - U: Boresight scan
  - D: Vertical scan
  - P: HMD sight
When using any CAC (dogfight) mode, you must press TDC press to lock.

Guns -- GSh-30-1 30 mm cannon, 150 rounds
1. Toggle gun with Gray Reset Hat back.
2. Radar will automatically lock targets in HUD, you might have to press TDC press to force a lock if it doesn't lock automatically.
3. Circle around pipper shows range, 0 to 1200 m.
4. Boxed number in bottom right of HUD shows remaining ammo in quarters:
  1. 4 = full
  2. 3 = 3/4 ammo remaining
  3. 2 = 2/4 ammo remaining
  4. 1 = 1/4 ammo remaining
5. Fire with Trigger.

Missiles
1. Cycle missiles with Lower Gray Button. Selected station is shown in bottom of HUD, missile type in lower right of HUD.
2. When you have Launch Authority (LA in bottom center of HUD), fire with Trigger.

Missile types
- R-73 (AA-11 Archer) -- IR, all aspect HOB
- R-27R/ER (AA-10 Alamo-A/C) -- SARH
- R-27T/ET (AA-10 Alamo-B/D) -- IR, all aspect??
- R-77 (AA-12 Adder) -- Active radar homing, J-11A only