501 - A/G - Stores List

Bombs:
- BetAB-500	Concrete piercing bomb, low-drag (no parachute or rocket)
- BetAB-500ShP	Concrete piercing bomb, high-drag (parachute and rocket)
  - Drop BetAB-500ShP between 150-1000 m
- FAB-250	GP HE bomb
- FAB-500 M62	GP HE bomb
- KMGU-2 - 96 AO-2.5RT	Submunition dispenser, frag
- KMGU-2 - 96 PTAB-2.5KO	Submunition dispenser, AP
  - Drop KMGUs between 50-150 m
- RBK-250 - PTAB-2.5M	Cluster bomb, AP
- RBK-250-275 - AO-1SCh	Cluster bomb, frag
- RBK-500 - PTAB-1M	Cluster bomb, AP
- RBK-500 - PTAB-10-5	Cluster bomb, AP
- RBK-500U - OAB-2.5RT	Cluster bomb, frag airbursting
  - Drop RBKs at 300 m minimum
- SAB-100	Illumination Bomb, drop between 1000-3000 m, Illumination lasts 1-5 minutes

Rockets:
- S-13 OF	122 mm, 5 rounds/pod, HE blast/frag warhead, 1.6-3.0 km range
- S-8OFP2	80 mm, 20 rounds/pod, 1.3-4.0 km range, HE blast/frag warhead
- S-8KOM	80 mm, 20 rounds/pod, 1.3-4.0 km range, HEAT warhead
- S-8TsM	80 mm, 20 rounds/pod, 1.3-4.0 km range, Smoke (often banned on servers due to lag issues)
- S-25 OFM	340 mm, 190 kg blast/frag warhead, 4 km max range
  - Fires one per trigger press, even with the double racks. Empty tubes cannot be jettisoned.