201 - Ground - Cold Start

Cold Start -- WIP
1. Flaps lever ... Up (left console)
2. Gear lever ... Down (left console, by floor)
3. Carb ram air control ... RAM AIR (forward) (left console under throttle??)
4. Trim ... Elevator: 0 if fuselage tank < 25 gal or 2-4 deg nose down if fuselage tank > 25 gal, Aileron: 0, Rudder: 6 deg right (left console)
5. Mixture ... Idle cutoff (throttle box)
6. Prop ... Full forward (throttle box)
7. Gyro ... Uncage
8. Parking brake ... Set
9. Supercharger ... Auto
10. Fuel shutoff valve ... On (center console between legs)
11. Fuel selector ... MAIN TANK LH (left wing tank) (center console between legs)
12. Fuel booster switch ... On (lower left instrument panel)
13. Battery switch ... On (right wall)
14. Generator switch ... On (right wall)
15. Oil and radiator flap switches ... On for all ground operations (will set to auto before takeoff)
16. Start engine:
  1. Ignition ... BOTH (top left of center console between legs)
  2. Throttle ... open 1 inch
  3. Primer switch ... Prime for 3-4 seconds if engine is cold, 1 second if engine is warm (lower left instrument panel)
  4. Starter switch ... START and hold (lower left instrument panel)
  5. As engine starts, move Mixture control to RUN and release START.
  6. Oil pressure should reach at least 50 psi within 30 seconds.
  7. Idle at 1300 to 1400 RPM until oil temp is 40 deg C and oil pressure is steady.
  8. After warmed up, idle at 1000 RPM.

Follow remaining steps in pre-flight checklist on following page.

Shutdown -- WIP
1. Prop RPM ... Full forward
2. Idle at 1500 RPM.
3. Fuel booster switch ... Off
4. Mixture ... Idle cutoff and open throttle as RPM drops below 700 RPM
5. Ignition switch ... Off
6. All electrical switches ... Off
7. Controls ... Locked
8. Carb air level ... UNRAMMED FILTERED AIR