202 - Ground - Preflight, Performance Limits

Preflight -- WIP
1. Flaps ... Full
2. If using external tanks: Fuel Tank Selector knob ... As needed (left console front)
3. Gun heat ... ON (switch on center console)
4. Pitot heat ... As needed (left console front, outboard of gear indicator, partly hidden)
5. Radios ... T/R or T/R+G (right console)
6. Takeoff trim ... Set (manually trim pitch until TAKE-OFF POS. IND. LATERAL–DIRECT LONGIT. light blinks briefly, top center of instrument panel)
7. Set up weapons ... As needed, see weapons pages. Common steps:
  1. Gun-Missile selector knob ... SIGHT CAMERA & RADAR (center console)
  2. Gunsight wingspan lever ... 30 ft (all the way left) (below gunsight)
8. Begin taxi; use NWS button (hold Flip Down Trigger) to steer at low speeds, differential braking at high speeds.

Performance limits
- Fuel: 2826 lbs internal
  - with 2x 120 gal drop tanks (801 lbs ea.) = 4428 lbs
  - with 2x 200 gal drop tanks (1335 lbs ea.) = 5497 lbs
- Engine modes:
Mode	MP	RPM	Time (minutes)	Critical alt Low/High SC
Takeoff	61	3000	5	n/a
WEP	67	3000	5	17,000 / 28,800
Mil power	61	3000	15	19,800 / 31,200
Max continuous	46	2700	Unlimited	20,500 / 34,400
Max cruise	42	2400	Unlimited	19,500 / 30,200

- Absolute max RPM (diving): 3240 RPM
- Minimum RPM:
  - Low supercharger: 1600 RPM
  - High supercharger: 2000 RPM
- Max airspeed IAS:
  - 0 to 5k ft: 505 mph (red line on airspeed indicator)
  - 5k to 10k ft: 480 mph
  - 10k to 20k ft: 400 mph
  - 20k to 30k ft: 300 mph
  - 30k to 40k ft: 260 mph
- Max diving speed IAS (due to compressibility):
  - 5k ft: 505 mph
  - 10k ft: 480 mph
  - 15k ft: 440 mph
  - 20k ft: 400 mph
  - 25k ft: 360 mph
  - 30k ft: 330 mph
  - 35k ft: 290 mph
  - 40k ft: 260 mph
- Landing gear: 170 mph or less
- Flaps speed IAS:
  - 10 deg: 400 mph
  - 20 deg: 275 mph
  - 30 deg: 225 mph
  - 40 deg: 180 mph
  - 50 deg: 165 mph
- Best glide speed: 175 mph IAS
- Clean stall speed: 94 to 106 mph depending on weight (heavier is faster)
- Landing config stall speed (gear down, flaps 45 deg): 87 to 101 mph (heavier is faster)
- Spin recovery: Ailerons with spin, rudder against spin, throttle at idle
- Automatic supercharger shift: 14,500 ft to 19,500 ft depending on airspeed (ram air)
- Tested max speed at sea level (50 ft) in ISA conditions, clean/no pylons, oil/air coolers auto:
  - Max continuous power: ~325 mph IAS (277 kts)
  - Full mil power: ~355 mph IAS (305 kts)