301 - Flight - Takeoff, Landing, Jettison

Taxi
Hold stick aft of neutral to engage tailwheel lock. While locked, rudder pedals steer tailwheel.

Takeoff
1. Canopy ... Close (T7 down)
2. Flaps ... Up for normal takeoff, or 15-20 deg for minimum takeoff run
3. Set max RPM (3000), smoothly throttle up to max takeoff power (61 in Hg).
4. Hold aft stick to keep tail down and tail wheel locked until rudder becomes effective.
5. Gently release aft stick pressure and let airplane fly up from the ground in 3-point attitude.
6. Gear up before 170 mph.
7. Flaps up before 275 mph.
8. Reduce power to max continuous (46 in Hg, 2700 RPM)
9. Best climb speed is 170 mph IAS.

Landing
1. Set 2700 RPM.
2. Below 170 mph, gear down.
3. Maintain 150 mph in traffic pattern.
4. (optional) Use 15 deg flaps for steeper approach.
5. When turning on final approach, lower flaps to full (under 165 mph)
6. Approach speed approx 115 to 120 mph IAS.
7. Cut throttle and flare, do a 3-point landing, approx 90 mph IAS.

Jettison
Cannot carry droptanks??