201 - Ground - Cold Start

Cold Start
Roof panel
1. AC POWER knob ... AC PHASE
2. DC POWER MAIN GEN switch ... ON and close switch cover
3. VM selector knob ... ESS BUS
4. BAT switch ... ON
Center console
1. LOW RPM switch ... OFF (next to guarded yellow FUEL switch)
2. FUEL switch ... ON (guarded yellow switch)
3. FORCE TRIM switch ... ON (center console front)
4. HYD CONT switch ... ON (center console front)
5. IFF MASTER knob ... STBY
Positions as noted
1. Doors ... Close (RCtrl-C if you can't click them)
2. Throttle ... Full back (Flaps lever)
3. Collective ... Full down
4. Throttle ... Idle position (must use mouse scroll on throttle: up to full, then back down to idle; the word "FRICTION" should be about centered at the top)
5. Starter switch ... Press and hold (Bottom Thumb Button)
  1. When engine RPM is 40% (GAS PRODUCER gauge), release Starter Switch.
  2. When engine RPM is 70%, slowly (several seconds) advance throttle to full.
  3. Rotor RPMs should eventually stabilize at lower end of green zone.
6. LOW RPM switch ... AUDIO (center console, next to guarded yellow FUEL switch)
7. INVTR switch ... ON MAIN (roof panel front)
8. STARTER GEN switch ... STBY GEN (roof panel front)
9. Radar Altimeter Power switch ... RADAR (roof panel rear)
10. Radar Altimeter gauge ... On and set low/high warning (left knob to turn on and set low, right knob to set high)

Proceed with preflight checklist on next page.