202 - Ground - Preflight, Radios, Performance Limits

Preflight
1. You may have to set the radio Intercom Mode knob to INT to communicate with the ground crew. When finished, set back to 2 for your main UHF radio (ARC-51BX)
2. Arm weapons ... As desired, see steps on other checklist
3. If in icing conditions:
  1. DE-ICE switch ... ON (center console, aft of guarded yellow FUEL switch)
  2. PITOT HTR switch ... ON (roof panel)
4. Radios ... As desired, see steps below.
5. Countermeasures Arm switch ... ARM, set number of flares (30 is default load) (center console rear)
6. IFF system ... ON, MASTER knob ... NORM (not implemented in the game)
7. Lights ... As desired (light switch panel on roof console)
8. Compass ... Syncronize (half way between o and +, matched to backup magnetic compass)

Performance limits
- Max achievable level speed: ~120 kts (~220 kph), depending on air pressure and temperature
- Max achievable fully loaded speed: ~95 kts (~175 kph)
- Climb speed: 60 kts
- Cruise speed: 80-90 kts
- Autorotation glide speeds (rotor RPM 295-340):
  - Minimum rate of descent (e.g. to allow time for engine restart): 55-65 kts, 1400-1800 fpm
  - Maximum glide distance (e.g. to get to a landing area): 80-90 kts, 1600-2400 fpm
- Vne speed: ~200 kts?? (~370 kph), due to retreating blade stall
- Exhaust Gas Temperature (EGT) limits:
  - Max Continuous: 610 deg C (top of the yellow??)
  - Takeoff power: 625 deg C, 30 minutes (yellow portion of EGT gauge??)
  - 10-second limit: 675 deg C, 10 seconds
  - 5-second limit: 760 deg C, 5 seconds
  - When over 645 deg C: 166 sec (2m46s) until engine degradation (RPM drop), 209 sec (3m29s) until engine fire
  - When over 680 deg C: 83-88 sec (1m23s-1m28s) until engine degradation (RPM drop), 90-95 sec (1m30s-1m35s) until engine fire