201 - Ground - Cold Start

Cold Start -- WIP but should be mostly complete
Autostart takes ~2m0s
1. Generator No. 1 ... ON (roof panel middle)
2. Generator No. 2 ... ON (roof panel middle)
3. Air Source switch ... APU (roof panel middle)
4. BATT swicch ... ON (roof panel middle)
5. Generator APU ... ON (roof panel middle)
6. APU Control switch ... ON (roof panel middle)
7. NAV MODE knob ... LAT/LONG (center console middle forward)
8. ENT (PAGE) button ... Press 2x (center console middle forward)
9. SAS1, SAS2, TRIM, BOOST buttons ... ON (center console middle)
10. Start engines:
  1. Fuel selector levers ... DIR (roof panel forward, levers with white knobs on throttle quadrant)
  2. Engine 2 Start button ... Press (roof panel forward, small button on throttle quadrant)
  3. Engine 2 Power lever ... IDLE
  4. Monitor engine start, engine should idle at 520 deg TGT and 630 Ng
  5. Engine 1 Start button ... Press
  6. Engine 1 Power lever ... IDLE
  7. Monitor enigne start
  8. When engines are started, power levers to FLY (fully forward)
11. Generator APU ... OFF (roof panel middle)
12. APU Control switch ... OFF (roof panel middle)
13. APR-39 power ... ON (turns on RWR) (center console rear left)
14. Radios ... On

Proceed with preflight checklist on next page.