301 - Flight - Radios, VRS Recovery

Radio setup and tuning
COM1	ARC-51BX	UHF	225.000 to 399.95 MHz	AM	"UHF" panel / left stack	Radio Selector 2
COM2	ARC-134	VHF	116.000 to 149.975 MHz	AM	"VHF COMM" panel / left stack	Radio Selector 3
COM3	ARC-131	LVHF	30.000 to 75.95 MHz	FM	"FM COMM" panel / right stack	Radio Selector 1
--	ARN-82	VHF	108.00 to 126.95 MHz	VOR	"NAV-COMM" panel / left stack	VOR receiver
--	ARN-83	LF/MF	190 to 1750 kHz	AM??	"ADF" panel / right stack	ADF receiver

All
On Signal Distribution Panel (center console), set Transmit/Interphone Selector knob to desired radio:
  - PVT: hotline
  - INT: Interphone (also communicates with ground crew)
  - 1: ARC-131 VHF FM (COM3)
  - 2: ARC-51BX UHF AM (COM1)
  - 3: ARC-134 VHF AM (COM2)
  - 4: not used
Set all radio knobs to T/R or T/R+G.

VRS Vuichard Recovery Technique for counter-clockwise rotor
1. Full left pedal (power pedal).
2. Right cyclic for 15-20 deg bank.
3. Raise collective slowly.