302 - Flight - Navigation

Navigate to an Emergency Locator Transmitter (ELT)
1. On ARC-131 radio panel (COMM), set frequency to 40.05.
2. Turn knob to HOME (homing)
3. Set Sensitivity Switch (next to Course Deviation Indicator) to HIGH.
4. Course Deviation Indicator will show direction of signal. You're flying toward it when the vertical line is aligned in the center.

Navigate to a beacon (FM Radio, NDB, VOR, ILS)
     VOR TACAN VORTAC VOR-DME NDB NDB-DME
Homing to FM radio station
1. On FM COMM panel (ARC-131 radio):
  1. Mode knob ... HOME
  2. Tune frequency with knobs.
2. CDI gauge shows needles (looks like ILS needles) in the direction to the signal.
  - Make sure you're flying toward the signal (and not directly away) by turning away from the needle; it should move in the opposite direction you turned.
NDB
1. On ADF radio panel (ARN-83 radio):
  1. Gain Control / Mode knob ... ADF (left/right click to cycle modes)
  2. Tune Control / Band Selection knob ... As needed (left/right click to change frequency range, scroll to tune frequency)
  3. Watch the signal strength needle above: left = weak, right = strong
2. Receiver NAV switch ... ON (row of switches above Intercom Mode knob)
3. VOR/ADF knob on compass ... ADF
4. Pointer on compass indicates direction to beacon.
VOR
1. NAV-COMM radio power knob ... PWR (left/right click to cycle power mode)
  1. Tune frequency by scrolling on knobs
2. VOR/ADF knob on compass ... VOR
3. Pointer on compass indicates direction to beacon.
4. To fly a specific radial course to/from the VOR, set course with OBS knob on CDI (below compass). Needles on CDI show course deviation.
5. TO/FROM triangle on lower right quadrant of CDI points up (TO) if flying on the selected course will take you toward the VOR; if the triangle points down (FROM), flying on the selected course will take you away from the VOR.. e.g. If you are on the 90 deg radial relative to a VOR, setting your CDI course to 270 will show TO, and setting your CDI course to 90 will show FROM.
ILS (click on runway icon to get window with ILS freq)
Same as VOR, but set the course on the CDI to be the runway heading.