1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

102 - Controls - Throttle Grip (A-10C II only)
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Top Hat -- "Countermeasures Switch (CMS)"
- F: 6 Chaff
- B: 6 Flares
- U: 1 Flare	L-U: Next program
- D: 1 Chaff	L-D: Previous program
- P: Toggle selected program	L-P: Toggle ECM
Top Hat Ring
- F: CMSP NXT rocker up (next CM program or increase value)
- B: CMSP NXT rocker down (previous CM program or decrease value)
Middle Hat -- "Mic Switch"
- U: (SRS radio 1 PTT)
- D: (SRS radio 2 PTT)
- F: (SRS radio 3 PTT)
Bottom Hat -- "Speed Brake Switch"
- F: Extend speedbrakes (keeps extending while held, stays open when you let go)
- B: Retract speedbrakes (keeps retracting while held)
Front/Rear Thumb Button -- "China Hat" (NOTE Needs testing, manual is inconsistent)
SOI->	TAD	TGP	HUD	AIM-9	Mav	HMCS	HMCS B/S	MSG
Fwd	--	FOV toggle	Change LSS FOV	Uncage	FOV toggle	TGP FOV toggle	--	--
Fwd-Long	Slave all to SPI			Slave to TGP	Slave all to SPI
Back	Reset cursor	LSS toggle	Cage TDC to VV	Cage, then Missile Step	Cage, then Missile Step	--	--
Back-Long	Slave TGP to steerpoint

Bottom Thumb Button
- P: Right throttle to idle detent (used for engine start)
- S-P: Left throttle to idle detent (used for engine start)
Ministick -- Slew Control
Axes: Slew
P: --
Middle Finger Hat -- "DMS (Data Management Switch)" (forward on real switch is up)
SOI->	TAD	TGP	HUD	AIM-9	Mav	HMCS	HMCS B/S	MSG
Up (fwd)	TAD scale decrease	Zoom and Focus increase	Steerpoint increment		B/S Reticle up	Brightness increase	Text Rotate CCW	Change Shape
Up-Long	(while held??) Map quick toggle				B/S Reticle up/Gyro stab			Drop Shape
Down (aft)	TAD scale increase	Zoom and Focus decrease	Steerpoint decrement		B/S Reticle down	Brightness decrease	Text Rotate CW	--
Down-Long	Select TAD Center Option							--
Left	CEN/DEP Mode, CNTR Own	RMFCD video on HMD	Gunsight toggle, Profile toggle		B/S Reticle left	RMFCD video on HMD	Boresight Roll CCW
Left Long	HMD on/off							HMD on/off
Right	Cycle TAD Center Option	Laser/IR pointer toggle	Gunsight toggle, Profile toggle		B/S Reticle right	Cycle HMCS profiles	Boresight Roll CW
Right Long	Slave TGP to HMCS				Slave Mav to HMCS	Slave TGP to HMCS		Slave TGP to HMCS

Ring Finger Slider
U/D: --
Pinky Switch -- "Boat Switch" (forward on real switch is up)
SOI->	TAD	TGP	HUD	AIM-9	Mav	HMCS	HMCS B/S	MSG
Up	TGP FLIR BHOT				Black symbols	TGP FLIR BHOT
Press	TGP CCD				Force correlate/Auto	TGP CCD
Down	TGP FLIR WHOT				White symbols	TGP FLIR WHOT

S-U/S-P/S-D: LAAP (autopilot) switch Path hold, Alt/Heading hold, Alt hold
Pinky Button -- "Left Throttle Button"
P: Toggle autopilot
Pinky Wheel -- "Pinky Switch"
- F: Default external lights
- B: Lights according to panel
- P: Exterior lights off