1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Basic Navigation, Jettison, Landing
Same for A-10C and A-10C II

Takeoff
Trim ... Set to Takeoff Trim with button outboard of throttle
  - Hold button until TAKE OFF TRIM light comes on.
1. Flaps ... MVR position (T6 switch forward/back, middle switch position in real cockpit)
2. Speedbrakes ... Retracted
3. Brakes will hold 100% throttle.
4. Begin takeoff run.
5. Disengage NWS at 70 kts (Flip-down Trigger press).
6. Rotate at 135 kts to 10 deg AOA and let it fly itself up off the runway.
  - Don't go over 13 deg or risk tailstrike.
Gear and flaps up. (Flaps will retract automatically at 185 kts if they're not up already.)

Basic Navigation (see other pages for adding/editing waypoints)
Waypoints/Steerpoints
In A-10 vocab, "steerpoint" is the currently selected "waypoint".
1. Select steerpoint with STEER rocker switch on UFC (left side of UFC).
2. Tadpole on HUD shows direction to steerpoint.
3. HUD shows more steerpoint information in lower right data stack:
  - 1st line shows radar altitude.
  - 2nd line shows current steerpoint number / name. Example: 2/BRIDGE is steerpoint 2, which is named "BRIDGE".
  - 3rd line shows distance.
  - 4th line shows ETE / TOT deviation.
  - 5th line shows current time.
HSI compass (center instrument panel, under artificial horizon) can also show bearing and distance:
  - On the outermost ring, pointer 2 always points to the steerpoint. (Pointer 1 points to TACAN, see below.)
  - Press STR PT button below HSI to show bearing and distance to steerpoint in the top corner readouts.
TACAN
1. TACAN panel is on right console inboard rear.
2. Use knobs to set channel and X/Y, turn Mode dial to T/R or A/A as needed.
3. HSI compass (center instrument panel, under artificial horizon) can show bearing and distance:
  1. On the outermost ring, pointer 1 always points to the TACAN station. (Pointer 2 points to the steerpoint, see above.)
  2. Press TCN button below HSI to show bearing and distance to TACAN in the top corner readouts.

Jettison -- WIP needs verification
1. On DSMS page, press SJET OSB (T4).
2. Press OSBs next to pylons to jettison.
3. Select jettison mode with T5 OSB: RACK, STR, or MSL.
  1. RACK jettisons the entire pylon and weapon rack, STR jettisons the stores only, and MSL fires a missile (Maverick or Sidewinder??) without arming or guiding.
4. Press Red Button to jettison. MASTER ARM must be ARM.

Landing -- WIP but should be basically accurate
1. Speed brakes at 40% out (no indicator, so guess).
2. Gear down below 250 kts.
3. Flaps full down below 185 kts.
4. 500 fpm descent rate.
5. No need to flare.
6. After stopping, retract airbrake, set flaps to HALF, and press Trim Reset button (Trim Hat Press).