1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing, AOA

Takeoff
1. Flaps ... 1/2 (gauge, left console front)
2. Pitch Trim ... As needed (dial, right console front) (medium load = 4 deg??)
3. Brakes will hold 90% RPM.
4. Begin takeoff run. Use differential braking to steer until rudder becomes effective, around 70 kts.
5. Rotate at 145 kts (line on airspeed indicator, faster if heavier). Rotate to about 10-15 deg and hold until airborne.
  - Don't get too fast on the ground or you'll pop a tire.
Flaps up and gear up by 225 kts.

Landing -- WIP
1. For shore landing: Spoiler ... ARM (left console forward)
2. For carrier landing: Hook ... DOWN
3. Open speed brake and keep open for landing.
4. Under 225 kts, gear and flaps down.
5. Onspeed AOA is 17.5 units. Maintain 160 kts minimum until short final. AOA indexer symbols:
  - ⋁ ... AOA too high, speed up
  - O ... On speed
  - ⋀ ... AOA too low, slow down
Touchdown around 125 kts, no flare needed (go Navy).

Landing with APC (Approach Power Compensator)
TODO...

Landing with ICLS (Instrument Carrier Landing System)
TODO...

AOA units
Assumes gross weight of 14,000 lbs. Add/subtract 0.35 units for each increase/decrease of 1,000 lbs.
Condition	With 2x 300-gal external tanks	Clean
Max climb	4.5 to 9.0	3.9 to 8.4
Max endurance	10.5	9.5
Cruise at 5,000 ft	6.6 to 7.0	6.0 to 6.4
Cruise at 35,000 ft	7.7 to 9.0	7.1 to 8.4