1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Radios, Navigation, Autopilot, Countermeasures, Jettison

Radios
TODO

Navigation -- WIP, needs verification
TACAN:
  1. TACAN controls are on right console middle.
  2. Tune channel with Channel Selector knob inner and outer (1s and 10s)
  3. No way to set X/Y?? X-band signals have priority over Y-band signals with the same number.
  4. Mode knob ... As needed. Use A/A for tankers, REC or T/R for other uses.
  5. BDHI (Bearing Distance Heading Indicator) switch ... TACAN (center) (instrument panel lower middle)
  6. Double-line needle?? on BDHI compass (instrument panel lower middle, below artificial horizon) shows bearing to TACAN station. Window in BDHI shows range.
Nav computer with doppler radar:
  1. Nav computer and doppler controls are on right console forward.
  2. First 2 waypoints from Mission Editor are pre-set (D1 = WP1, D2 = WP2, also shown in built-in kneeboard page)
  3. Set doppler radar knob (forward knob) to STBY at startup, then LAND or SEA as needed.
    - If doppler is OFF, you will need to input magnetic variance, wind direction, and wind speed manually.
    - Limits for doppler radar:
      - 30 deg up/down pitch, and left/right bank
      - 40 ft min altitude
      - When outside of limits, MEMORY light will illuminate, and position may drift.
  1. Set Function Select knob (rear knob) to STBY.
  2. PRESENT POSITION windows should show your current lat/long, adjust if needed.
  3. DESTINATION windows should show D1.
  4. Set Function Select knob (rear knob) to D1 or D2 to navigate to waypoint.
  5. BDHI (Bearing Distance Heading Indicator) switch ... NAV CMPTR (up) (instrument panel lower middle)
  6. Double-line needle?? on BDHI compass (instrument panel lower middle, below artificial horizon) shows bearing to waypoint. Window in BDHI shows range.

Autopilot
TODO

Countermeasures and ECM
- Default CM program:
  - 8 salvos of 1 burst, every 2 seconds, from any active dispensers.
  - Select which dispenser(s) will fire the salvos with switch on countermeasures box on upper left outer instrument panel.
    - Front dispenser (#1) is always chaff, rear dispenser (#2) is always flares.
  - Program using built-in kneeboard page. Engine must be OFF and canopy OPEN.
  - Default load is 30 chaff, 30 flares.
- RWR and ECM systems -- WIP
  - APR-25 is RWR (E-, G-, and I-band only) and ECM.
    - Detects radar signals and turns them into audio.
    - Volume controlled by inner knob.
    - RCV mode does not jam. RPT mode will jam when radar signals are detected.
  - APR-27 is SAM Launch Warning Receiver (SA-2 only??)
    - Detects missile guidance signals only.
    - Volume controlled by outer knob.
  - AUDIO switch:
    - Not sure what this does..??

Stores Jettison
Select station to be jettisoned with EMER SEL knob (center console top left):
  - WNG ... Jettisons stations 1, 2, 4, 5 (wing stations)
  - 1, 2, 3, 4, 5 ... Jettisons only numbered station.
  - AL ... Jettisons all stations.
Pull EMER BOMB handle (above left knee) to jettison selected station.