1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - Guns, Gun pods, AIM-9 Sidewinders

Fence In:
Master Arm ... ON

Internal guns -- 2x Mk 12 20 mm cannon, 100 rounds each, 1000 rpm
GUNS switch ... READY (charges guns, should make an audible "clunk") (center console top)
  - You have 3 nitrogen charges to arm the guns. Those get refreshed when doing Rearm/Refuel.
1. Gunsight depression ... 0 mils
2. Fire with Trigger.
  - If gun pods are also armed, they will fire as well.

Gun pods -- Mk 4 HIPEG 20 mm cannon, 750 rounds each, 1000 rpm
1. GUN PODS station switches ... READY for stations with gun pods (left console forward, just in front of throttle)
2. CHARGE switch ... CHARGE (right-click) (left console forward, just in front of throttle)
  - Keep them in CHARGE to use the gun pods.
  - If gun pods are set to CLEAR, they will be cleared and rendered inoperable until Rearm/Refuel.
  - You have 3 nitrogen charges to arm the guns. Those get refreshed when doing Rearm/Refuel.
1. Gunsight depression ... 0 mils
2. Fire with Trigger.
  - If internal guns are also armed, they will fire as well.

AIM-9 Sidewinders
Station Selector switches ... READY for stations with Sidewinders (center console top)
  - Only select stations with Sidewinders.
Weapon Function Selector knob ... BOMBS & GM ARM
  - You should hear a Sidewinder tone. If you have stations selected with other weapons, you won't get tone.
  - Adjust volume with Shrike/Sidewinder Volume knob (instrument panel bottom center, inner knob)
1. Put gunsight near target, wait to get high-pitched growl.
2. When you have tone, seeker will automatically uncage to follow target.
  - When you hit the gimbal limit, it'll unlock and return to caged in the center.
  - There is no manual cage/uncage.
Press Red Button to fire.

General dogfighting tips -- TODO
- Best turn performance at xxx kts.
- Don't go under xxx kts.