1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Guns, Gun pods, Rockets

Fence In:
Master Arm ... ON

Internal guns -- 2x Mk 12 20 mm cannon, 100 rounds each, 1000 rpm
GUNS switch ... READY (charges guns, should make an audible "clunk") (center console top)
  - You have 3 nitrogen charges to arm the guns. Those get refreshed when doing Rearm/Refuel.
1. Gunsight depression ... 0 mils
2. Fire with Trigger.
  - If gun pods are also armed, they will fire as well.

Gun pods -- Mk 4 HIPEG 20 mm cannon, 750 rounds each, 1000 rpm
1. GUN PODS pylon switches ... READY for pylons with gun pods (left console forward, just in front of throttle)
2. CHARGE switch ... CHARGE (left console forward, just in front of throttle)
  - Keep them in CHARGE to use the gun pods.
  - If gun pods are set to CLEAR, they will be cleared and rendered inoperable until Rearm/Refuel.
  - You have 3 nitrogen charges to arm the guns. Those get refreshed when doing Rearm/Refuel.
1. Gunsight depression ... 0 mils
2. Fire with Trigger.
  - If internal guns are also armed, they will fire as well.

AWRS panel setup for rockets
- QTY SEL knob (left): Sets how many pulses will be sent while pickle is held in RIPPLE mode. OFF = 1.
- DROP INTVL (center): Sets the interval between the pulses.
  - MULT switch controls whether interval is in milliseconds as shown (X1, up), or in tenths of a second (X10, down).
  - E.g. 50 with MULT=X1 drops every 0.050 secs; with MULT=X10, drops every 0.50 secs.
- MODE SEL knob (right):
  - Settings on left side of knob (STEP) sends 1 pulse per pickle press. Ignores QTY SEL.
  - Settings on right side of knob (RIPPLE) sends number of pulses up to QTY SEL while pickle is held.
  - Pulses are distributed to stations as follows:
    - SINGL ... Rocket pods fire one at a time. Rocket pods on the same station fire alternately.
    - PAIRS ... Rocket pods fire on paired stations simultaneously. Rocket pods on the same station fire alternately. Centerline station will not fire anything in this mode.
    - SALVO ... All rocket pods fire simultaneously. Rocket pods on the same station both fire.

Rockets
Gunsight depression ... As needed
  - 0 mils works for steep diving attacks or close range, otherwise see depression table in built-in kneeboard.
1. Bomb ARM switch ... TAIL or NOSE & TAIL
2. Station Selector switches ... READY for stations with rocket pods
3. Weapon Function Selector knob ... GM UNARM (recommended) or ROCKETS
  - If in GM UNARM, fire rockets with Red Button and gun with Trigger.
  - If in ROCKETS, fire rockets with Trigger. If gun is armed, gun will also fire.
  - (If in BOMB & GM ARM, entire rocket pods will be pickled off the plane if stations are selected.)
1. AWRS setup ... As desired, see above
2. Fire with Red Button if in GM UNARM, or fire with Trigger if in ROCKETS, which will also fire guns if armed.