1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Unguided Bombs

Fence In:
Master Arm ... ON

AWRS panel setup for bombs
- QTY SEL knob (left): Sets how many pulses will be sent while pickle is held in RIPPLE mode. OFF = 1.
- DROP INTVL (center): Sets the interval between the pulses.
  - MULT switch controls whether interval is in milliseconds as shown (X1, up), or in tenths of a second (X10, down).
  - E.g. 50 with MULT=X1 drops every 0.050 secs; with MULT=X10, drops every 0.50 secs.
- MODE SEL knob (right):
  - Settings on left side of knob (STEP) sends 1 pulse per pickle press. Ignores QTY SEL.
  - Settings on right side of knob (RIPPLE) sends number of pulses up to QTY SEL while pickle is held.
  - Pulses are distributed to stations as follows:
    - SINGL ... Bombs drop one at a time, alternating selected left/right/center stations.
    - PAIRS ... Bombs drop from paired stations simultaneously. Centerline station will not drop anything in this mode.
    - SALVO ... Bombs drop from all selected stations simultaneously.

Bombs with CMPTR -- CCRP mode, for slick bombs and cluster bombs, not Snakeyes
1. Radar altimeter ... ON
2. Radar knob ... A/G (Mode knob on throttle) (left console middle)
  - You can leave the radar ANGLE OF ATTACK COMP switch ON (left console middle).
1. Gunsight depression ... 0 mils
2. Bomb ARM switch ... TAIL or NOSE & TAIL
3. Station Selector switches ... READY for stations with bombs
4. Weapon Function Selector knob ... CMPTR (B1 and B3 buttons to rotate) (center console top)
5. AWRS setup ... As desired, see above, RIPPLE mode recommended (see below) but not required
6. Dive at target, wings level, no yaw. Feet off rudder pedals! Does not correct for roll, yaw, or wind.
7. Radar should establish a ground lock, shown by a stationary horizontal line on radar screen.
8. Put pipper on target, press and hold Red Button. LABS light below gunsight should illuminate and tone will sound.
9. Keeping wings level, pull up slowly until bombs release.
  - If in STEP mode, light and tone will continue until pickle button is released.
  - If in RIPPLE mode, light and tone will stop when ripple is complete and all bombs have dropped. This is why RIPPLE is recommended.
Tested with Mk-80 series slicks and Mk-20 Rockeyes, and accuracy is reasonable. Steeper dives and lower releases are more accurate. Use ripple strings to compensate.

Bombs with manual bombsight
1. Gunsight depression ... As needed, see depression tables in built-in kneeboard
2. Bomb ARM switch ... TAIL or NOSE & TAIL
3. Station Selector switches ... READY for stations with bombs
4. Weapon Function Selector knob ... BOMBS & GM ARM
5. AWRS setup ... As desired, see above
6. Press Red Button to drop.

Bomb interval spacing table and notes
- Intervals	0.06 sec	0.10 sec	0.14 sec
  600 kts	60.8 ft	101.3 ft	141.8 ft
  550 kts	55.7 ft	92.8 ft	130.0 ft
  500 kts	50.6 ft	84.4 ft	118.1 ft
  450 kts	45.6 ft	76.0 ft	106.3 ft
  400 kts	40.5 ft	67.5 ft	94.5 ft
  350 kts	35.4 ft	59.0 ft	82.7 ft
- Calculation: kts / 60 / 60 * 6076.115 / interval = distance in ft
Snakeye
- 80 mils, 200 ft, 500 kts?
- Dropping in ripple can blow up your own plane, possibly due to the bombs hitting each other, or maybe hitting the plane. Interval of 0.14 can help, and making sure you're not pushing anything less than 1 G, but it's not reliably safe with any settings.
CBU
- Seems to burst after a set amount of time. In level flight, drops at 450 to 500 AGL burst before they hit the ground and give a decent scatter. But in a dive, dropping from that height makes them hit the ground before bursting.
- Scatter is not affected by altitude (bug).