1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - CBU dispensers

Fence In:
Master Arm ... ON

Name	Type	Number of bomblets	Possible tubes/pulse (default)
CBU-1/A	Antipersonnel	101	(2)
CBU-2/A	Antimaterial	72	(1), 2, 3, 4, 6, 17
CBU-2B/A	Antimaterial	81	(2), 4, 6

Dispensers - CBU-1/A, CBU-2/A, CBU-2B/A
Set tubes/pulse in the kneeboard based on how many bomblets you want per pulse. See below for calculations. 1 tube/pulse = 5 bomblets, 2 tubes/pulse = 10 bomblets, etc.
  - Engine must be off to change tubes/pulse.
1. Bomb Arm switch ... NOSE & TAIL or TAIL
2. Function Selector knob ... BOMBS & GM ARM
3. Pylon switches ... As needed
4. Drop from very low altitude in level flight or very shallow dive. Pickle approx when target is halfway between gunsight center and bottom??

CBU-2B/A -- 81 bomblets per pylon (single racks):
- 3 drops (actually 2.7): 6 tubes/pulse, AWRS qty OFF, Ripple Pairs, interval doesn't matter.
- 2 drops (actually 2.025): 4 tubes/pulse, AWRS qty 2, Ripple Pairs, shortest possible interval (unless you want a longer string), leaves 1 bomblet left in each container.
CBU-2B/A, 162 bomblets per pylon (dual racks):
- 3 drops (actually 2.7): 6 tubes/pulse, AWRS qty 2, Ripple Pairs, shortest possible interval.
- 2 drops (actually 2.025): 4 tubes/pulse, AWRS qty 4, Ripple Pairs, shortest possible interval (unless you want a longer string), leaves 1 bomblet left in each container.

Calculating the number of drops:
1. bomblets/container * containers/pylon = bomblets/pylon
2. 5 * tubes/pulse = bomblets/pulse
3. bomblets/pulse * AWRS qty = bomblets/drop
4. bomblets/drop / bomblets/pylon = total number of drops

Example, CBU-2B/A dual racks:
1. 81 bomblets/container * 2 containers/pylon = 162 bomblets/pylon
2. 5 * 6 tubes/pulse = 30 bomblets/pulse
3. 30 bomblets/pulse * 2 AWRS qty = 60 bomblets/drop
4. 60 bomblets/drop / 162 bomblets/pylon = 2.70 drops

Misc notes:
- With 2 pylons selected, in Step Single, each pickle press drops 1 pulse (5 bomblets) from 1 pylon, the next press drops from the next pylon, then back to the first, alternating.
  - With Step Pairs and Step Salvo, each pickle press drops 1 pulse from both pylons.
  - Seems to ignore interval setting.
- With 2 pylons selected, in Ripple Single, each pickle press drops 1 pulse, always dropping from the same pylon until that pylon is empty, then switches to the other pylon and drops from there.
  - AWRS quantity selector sets number of pulses sent. Ripple Single drops from one pylon until empty. Ripple Pairs alternates pylons, Ripple Salvo drops from all pylons. Interval knob sets interval between pulses.
- Use AWRS quantity selector to set number of pulses