1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504 - A/G - AGM-45 Shrike

Fence In:
Master Arm ... ON

AGM-45 Shrike
1. Weapon Function Selector knob ... BOMBS & GM ARM
2. Station Selector switches ... READY for stations with AGM-45 Shrikes
  1. You should hear a Shrike tone, similar to a Sidewinder.
  2. Adjust volume with Shrike/Sidewinder Volume knob (instrument panel bottom center, inner knob)
3. AWRS setup ... STEP, SINGL
4. Aim at target area. Shrike has a 3 deg seeker radius (~53 mils; gunsight markings are 10 mils, so just larger than the middle circle on the sight).
5. When you get a high tone similar to a Sidewinder lock-on growl, seeker is locked.
6. Press Red Button to fire.