1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

300 - Flight - Aircraft Info, Performance Limits

Aircraft Info
Fuel:
	100%	90%	80%	70%	60%	50%	40%	30%	20%	10%
Internal	2513	2262	2010	1759	1508	1257	1005	754	503	251
Robbie tank	3170	2853	2536	2219	1902	1585	1268	951	634	317

  - With Robbie tank installed, 79% internal fuel is empty Robbie tank and full internal fuel.
  - External fuel tanks: 1548 lbs of fuel each (total full weight 1688 lbs, empty weight 140 lbs)
- Tested max fully loaded speed (with 8x Hellfire + 2x M151 rocket pods): 132 kts (244 kph) in nose-to-tail trim, 134 kts (248 kph) in aerodynamic trim
- Vne speed: 197 kts, or less depending on density altitude and temperature. Shown on PERF page.
- Max achievable speed about 210 kts (388 kph) in a steep dive, no retreating blade stall happening.

Performance limits
- Speeds:
  - With symmetrical external tanks: 130 kts
  - Stores jettison: 130 kts (minimize side slip); external tank jettison: 100 kts
  - Sideways/backwards flight: 45 kts
  - Searchlight: Moving light: 90 kts; Not moving: 200 kts
- NR limits (rotor RPM):
  - Max: 110%
  - Transient: 106-110% (high rotor warning light at 106+%)
  - Normal: 95-105%
  - Transient: 0-94%
- TGT limits (T700-GE-701C engine):
  - Max: 949 °C
  - Single engine transient: 897-949 °C, 12 sec
  - Single engine contingency: 879-896 °C, 2.5 min
  - Intermediate rated power: 871-878 °C, 10 min
  - Maximum during start: 851 °C
  - Intermediate rated power: 811-870 °C, 30 min
  - Max continuous: 810 °C
  - Normal: 0-810 °C
- Torque limits:
  - Rated Max: 115% (actual max is 130%)
  - Transient: 101-115% (6 sec)
  - Normal: 0-100%