1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304a - Flight - Datalink General Info and Primary (TSD page)

General Info
- Datalink "Presets" are pre-defined groups of helicopters. The helicopters in a given Preset can share data with other helicopters in that same Preset. You can change to a different Preset in flight.
- Each Preset has a Unit ID, a Call Sign, and a Primary Freq (a specific radio, either VHF, UHF, FM1, or FM2). Default settings:
Preset	Unit ID	Call Sign	Primary Freq
1	PRESET 1	PRE 1	VHF SC
2	PRESET 2	PRE 2	UHF SC
3	PRESET 3	PRE 3	FM1 SC
4	PRESET 4	PRE 4	FM2 SC
n...10	PRESET n...PRESET10	PRE n...PRE10	no default radio assigned

- Helicopters in a Preset can be a Primary, a Team Member, or both.
  - A Primary can send/receive Reports and Points through TSD.
  - A Team Member can send/receive Messages and Mission data through COM page.
  - The Preset as configured on your helicopter can have different Primary/Team Members than the configuration for the same Preset on other helicopters.
- Every helicopter on a given Preset must have a unique Originator ID (and Callsign??).
- Each Preset can have up to 10 aircraft assigned to it.
- Select which Preset (and therefore radio??) to transmit on by using the IDM rocker on the left of the EUFD.
- COM page shows the Presets.
- To configure a Preset on the COM page:
  - Box the desired Preset OSB with L1-L5 or R1-R5 OSBs.
  - B6 OSB PRESET EDIT to go to a page with more details on the Preset including the Unit ID, Call Sign, etc.
  - Assign a radio to the Preset by selecting T1-T5 OSBs, then B6 OSB to set SC (Secure Channel) or B4 OSB to set FH (??).
- Change your ownship Originator Id and Callsign with ORIG ID OSB.
- To change who is assigned to one of your Presets, select a Preset then press NET OSB. Then select an assigned aircraft (L1-L5/R1-R5 OSBs), then top OSBs: DEL to unassign, or box/unbox TEAM or PRI to set those.
- To add an aircraft, press MBR DIR OSB, then REPLACE or ADD OSBs (use REPLACE if you're already at 10 assigned??

Sending data on TSD
- Send your Present Position (PP):
  - Press RPT OSB (T1 OSB), then PP OSB (L3 OSB), box who you want to send it to (callsigns shown on other OSBs, all will be boxed by default), then SEND OSB (R6 OSB).
- Send a request for other aircraft PP:
  - Press RPT OSB (T1 OSB), then PP OSB (L3 OSB), B2 OSB to change from SEND to REQ, box who you want to send it to (callsigns shown on other OSBs, all will be boxed by default), then SEND OSB (R6 OSB).
- Point (waypoint, targetpoint, etc.)
  - Select point on TSD (POINT OSB, then either use cursor or enter name of point on L1 OSB), then XMIT OSB (L6 OSB), box who you want it to send to, then SEND OSB.

Receiving data on TSD
- When data is sent, L2 OSB will show REC. Press to show data, then press corresponding OSB for received data you want to show.
- Request PP from other flight members:

Datalink setup -- WIP
- Your DL ID is shown on the COM page in the OWNSHIP box.
- Change your DL ID by pressing ORIG ID OSB, then DATALINK ORIG ID OSB (R1 OSB), and enter a new ID (1-9) on the keyboard, then press enter.
- You can also change the PRESET (radio freq, radio type, and other settings).
- Edit who is assigned as Primary/Team Member with NET OSB.
  - Add with MBR DIR OSB (L6 OSB).
  - Remove by selecting member on left, then DEL (T2 OSB), then YES OSB.