1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

306 - Flight - Navigation to NDB

Navigate to a beacon (NDB) with ADF (AN/ARN-149) -- WIP, needs verification
1. Set ADF audio if needed on CMWS control panel with CMWS/NAV switch to NAV (PLT front right canopy frame)
2. Go to TSD page -> INST (L1) -> UTIL (T6).
3. Press ADF OSB (B6) to toggle ADF power on, then UTIL to exit back to the INST menus.
4. Select ADF frequency, from TSD -> INST:
  - Manual tuning:
    1. Press FREQ> OSB (L3), enter frequency on KU and press ENTER.
      1. Press TUNE OSB (T5) to tune the ADF to the frequency.
    2. Press LAST FREQ OSB (L5) to toggle back and forth between current and previous frequency, useful when navigating to intersection??
  - Use a preset:
    1. Press UTIL OSB.
    2. Press L2-L6 or R2-R6 OSBs. (Presets may only have values for Caucaucus map??)
  - Edit a preset:
    1. Press UTIL OSB.
    2. Select preset to edit.
    3. Press ID> OSB (B4), enter Morse identifier on KU and press ENTER.
    4. Press FREQ> OSB (B5), enter frequency on KU and press ENTER.
    5. Press TUNE OSB (T5) to tune the ADF to the frequency.