1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - General procedures and communications

Sight, Acquisition Source, and Range Source
- Sight -- The selected weapon-aiming device. Weapons are pointed where the Sight is pointed, and fly to the target the Sight is aimed at. Sights are selected with the Sight Select Switch (Middle Hat on collective, or Bottom Hat on throttle). Approximately equivalent to the SOI in other aircraft. List of Sights:
  - HMD -- PLT or CPG Helmet-Mounted Sight.
  - TADS -- TADS sensor on the nose, controlled by gunner.
  - FCR -- Fire Control Radar (if equipped).
- Acquisition Source -- The selected point of interest for the sights. The TADS and FCR Sights can be slaved to the Acquisition Source, and the HMD Sight gets cuing information (broken cross) showing where the Acquisition Source is pointing. The Acquisition Source can be a fixed point (e.g. a waypoint) or a moving point (e.g. the LOS of the HMD or TADS). Acquisition Sources are selected with the ACQ or CAQ OSBs on the TSD, WPN, or FCR pages. Approximately equivalent to the SPI in other aircraft. List of Acquisition Sources:
  - PHS -- Pilot's HMD.
  - GHS -- Copilot/Gunner's HMD.
  - SKR -- Missile seeker LOS.
  - RFI -- Highest priority RWR azimuth.
  - FCR -- Next-to-shoot target detected by Fire Control Radar (if equipped).
  - FXD -- Fixed forward on aircraft centerline at -4.9 deg elevation.
  - TADS -- TADS LOS.
  - WXX, CXX, TXX (Waypoints) -- Nav/target waypoints (e.g. W01, C51, T01)
- Note: The Sight and the Acquisition Source cannot be the same in the same seat. E.g. if in the PLT seat, and the Sight is FCR, the Acquisition Source cannot be the FCR. However the CPG can set FCR as the Acquisition Source.
- Range Source -- The source of ranging information to whatever the Sight is looking at. Ranging can come from the Sight itself (e.g. the laser from the TADS, the FCR's radar range, or the LOS angle of the HMD), but is not necessarily coupled to where the Sight is looking. List of Range Sources:
  - Laser -- The laser range to the TADS LOS. Displayed as *XXXX (m) on the HAD. * = Laser is firing.
  - Radar -- The radar range from the FCR. Displayed as RX.X (km) on the HAD.
  - Navigation -- The range to a waypoint. Displayed as NXX.X (km) on the HAD.
  - Automatic -- A triangulated range based on radar altitude. Displayed as AXX.X (km) on the HAD.
  - Manual -- A manually-entered range. Displayed as MXX.X (km) on the HAD.
  - Default -- If range cannot be computed, PLT defaults to 1.5 km and CPG defaults to 3.0 km range.

How-to
- As PLT, see what the gunner is seeing through the TADS:
  - On either MFD, press VID, then TADS (R1), then TADS (T6). L1-L3 control a digital zoom of the image (doesn't affect what the gunner is seeing).
- As CPG, have your IHADSS up without showing the TADS FLIR/TV image, but still show the rest of the symbology (useful for still being able to look out and slave to LOS but without having the picture get in the way):
  - Select HMD as Sight (Bottom Hat up), then turn down BRT (brightness) on the TEDAC unit all the way to turn off the background video. Then select TADS as Sight (Bottom Hat forward), and the brightness on the IHADSS will stay off, while the BRT rocker now controls the TEDAC image.
- As PLT, enable the automatic nose pitch down for better visibility at low speed:
  - FLT page -> UTIL -> NOE/A (NOE/Approach). Nose will pitch down significantly while <80 kts. Turn off NOE/A mode by repeating these steps, or press Stabilator Reset on collective (Coll. shift-Index Finger Hat press).

Target acquisition and handoff flow and terminology -- WIP
General Apache terminology:
"WASing" weapons = selecting weapons
Pilot has visual target:
1. Gunner requests "PHS handover" to target spotted by pilot.
2. Pilot looks at target: "My line of sight, X targets or target tank/AAA/vehicle/etc."
3. Gunner slaves sight, then deslaves and calls "Deslaved".
4. Gunner is now cued on target.
5. Gunner lases and stores the target, calls "I have lase and store".
Gunner has visual target:
1. Pilot selects HMD with Sight Select Switch and TADS or GHS as Acquisition Source.
2. HMD crosshair shows cuing dots indicating where TADS is pointing or where Gunner is looking.