1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - Longbow FCR modes and use

General information
- Max range is 6 km for stationary targets, 8 km for moving targets.
- Up to xxx?? targets can be displayed at once.
- Next-To-Shoot (NTS) target has a diamond around it, Alternate-NTS (ANTS) has an upside-down triangle around it.
  - If drawn with a dashed line instead of solid, means RF Hellfire is not selected or ready.
- To change prioritization scheme:
- Press UTIL OSB (T6 OSB) on FCR page.
- Press SCHEME OSB (R4 OSB), then A, B, or C (L1-L3 OSB) to select scheme.
  - A = Prioritizes by threat, fixed or moving targets, no air targets.
  - B = Prioritizes by threat, fixed targets only, no air targets.
  - C = Prioritizes by threat, moving targets only, including air targets.
- Cycle through NTS targets by pressing NTS OSB (L1 OSB).
- Manually set NTS target by moving TDC cursor over target and pressing TDC press.
- Targets that have been shot at show a faint X behind the target. FCR will still prioritize shot-at targets and select them as NTS/ANTS.
- Power on radar:
  - FCR?? page > UTIL > MMA, change from PINNED to NORM. Then press L3?? OSB for FCR to turn it on. Then press FCR BIT OVERRIDE OSB.
- Radar cues toward your selected ACQ (Acquisition) source. If set to PHS (Pilot Helmet Sight), it will point to where you're looking. If set to TADS, will point to the TADS target (if any). If set to FXD (Fixed), will point straight ahead. If radar is manually slewed right or left (or back to center) it will remain fixed until the ACQ source is re-set (either to the same source or another one).
- Radar scan width and direction cannot be changed while radar is transmitting.

Target icons (see Dash 10, p. 674)
Type	LOAL	LOBL stationary	LOBL moving
Tracked
Wheeled
Air Defense
Unknown
Merged Air Defense
Helicopter
Fixed Wing	--	--