1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

507b - A/G - AGM-114K Hellfire other modes, Laser codes

Fence In:
- Master Arm ... ARM
- TSD ... ATK phase
- Laser ... Armed (CPG WPN page -> CHAN -> UTIL -> LASER)

Tested ranges from 50 ft AGL hover -- Min laser range is 500 m, max is 9.999 km
Mode	Traj	Min	Max
LOAL	HI	3.8 km	9.4 km
LOAL	LO	3.8 km	9.3 km
LOAL	DIR	??	??
LOBL	n/a	750 m	9.3 km

Remote lasing -- WIP
Same as self-designating, but set the missile code to the buddy lase frequency.

Ripple firing with FCR (not implemented yet)
TODO

Priority Fire Zone (PFZ) and wingman engagement (not implemented yet)
TODO

Hellfire and TADS laser codes
- You have 16 letters (A-R, except I and O), which are saved preset laser codes.
  - To edit the codes: WPN > CODE > FREQ, select letter OSB, enter new code on KU, press ENTER.
- Hellfires use Channels:
  - Set channel letters with WPN > CHAN, select channel at top, then letter for channel on sides and bottom.
  - You have 4 channels (1-4), which are each set to a letter (A-R).
  - One of your 4 channels is the PRI (Primary), and another is the ALT (Alternate). PRI is your main and will be used most of the time; ALT is only used for ripple fire mode, where it will alternate with PRI for each missile fired.
  - Set the PRI and ALT letters with WPN > PRI or ALT OSB, then select channel number to be assigned to that slot.
  - Normally, you set one letter as your PRI and another letter as your ALT. Your wingman sets your ALT as his PRI, and vice versa.
  - You can set your other 2 channels as you wish (e.g. to a JTAC code).
- TADS (laser designator) uses the letters:
  - Set laser code with WPN > CODE, then select letter OSB. Toggle setting LRFD (Laser Range Finder Designator, default) and LST (Laser Spot Tracker) with SET OSB.
  - Normally, your TADS should be set to the same letter as your PRI, so you can self-designate your missiles.

Set LST (Laser Spot Tracker) code
WPN page > CODE OSB > SET OSB (T2 OSB) to toggle LRFD/LST > Select code with OSB.