1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

508 - A/G - AGM-114L Hellfire

Fence In:
- Master Arm ... ARM
- TSD ... ATK phase
- Laser ... Armed (CPG WPN page -> CHAN -> UTIL -> LASER)

Tested ranges from 50 ft AGL hover -- Min laser range is 500 m, max is 9.999 km
Mode	Min	Max
LOAL	??	??
LOBL	750 m	9.3 km

AGM-114L Hellfire II active radar setup and general info
- Radar Hellfire modes -- There are 2 modes, which the missile determines for itself:
  - LOBL -- If the target is closer than 2500 m or is moving.
  - LOAL -- If the target is farther than 2500 m and is stationary.
  - (You can use LOBL INHIBIT on WPN page to force LOAL mode.)
1. Set up options on WPN page (WPN OSB):
  1. TYPE (R1 OSB) ... RF for radar-guided Hellfires
  2. MODE (R2 OSB) ... NORM for normal missile sequencing
    - MAN is for manual using missile step button
  1. LRFD (R5 OSB)
    - FIRST ... Selects first laser rangefinder reflection for ranging.
    - LAST ... Selects last laser rangefinder reflection for ranging.
  1. LOBL INHIBIT ... If boxed, forces LOAL mode, missile radar will not go active until launched.
  2. 2ND TARGET INHIBIT ... TBD, used with FCR.

Engaging targets using TADS
1. Designate target with TADS and begin lasing (diagonal lines appear in the TADS crosshairs).
2. Continue lasing until "TARGET DATA?" on TADS disappears (3-4 seconds).
  - After "TARGET DATA?" disappears, the target is designated to that missile. If you want to select a different target, you must de-select (de-action/de-WAS) the Hellfires, then re-select them.
1. The missile constraints box will be small for a LOAL shot, large for a LOBL shot.
2. When the missile constraints box is solid, press and hold Trigger to fire.

PLT engage targets using FCR
Select FCR as Sight with Coll. Middle Hat left.
  - Recommended to set ACQ source to FXD, otherwise the radar may point in unintended direction.
Select RF Hellfire as weapon with Gray Reset Hat left.
  - FCR must be the active Sight in order to select RF Hellfire, otherwise it'll select SAL Hellfire.
1. Scan for targets with Coll. Trim Hat forward for single scan or back for continuous scan.
2. When targets are detected, system should automatically designate one as the Next-To-Shoot (yellow diamond), or you can manually designate with TDC ministick and press.
3. The missile constraints box will be small for a LOAL shot, large for a LOBL shot.
4. When the missile constraints box is solid, press and hold Trigger to fire.

CPG engage targets using FCR
TODO