1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Autothrottle

Takeoff
1. Make sure LS is the selected waypoint.
2. Verify correct departure runway in nav system (if using road base, you must set this manually):
  1. Data Selector knob ... BANA GRÄNS, OUT (Runway Heading)
  2. First 4 digits are runway heading in NNN.N format, last 2 digits are ILS channel (if available).
  3. To toggle to the reciprocal runway, press LS/SKU.
  4. To set custom heading:
    1. Data Selector knob ... BANA GRÄNS, IN
    2. Enter runway heading as 4-digit number, NNN.N deg and "00" at the end.
    3. Press LS/SKU, then set AKT POS, OUT.
3. Line up on the runway. If strong crosswind will cause you to deviate more than 15 degrees from runway heading on takeoff, press Reference Button (Lower Gray Button) to make the nav computer apply an offset based on your actual takeoff heading.
4. Brakes will hold full Mil power.
5. Use Mil power for takeoff if light, AB stage 2 or 3 if heavy.
6. Watch distance line at bottom of HUD, it should widen as you accelerate, and rotate when it reaches the vertical markers at the sides (around 250 kph).
7. Put Velocity Vector level with the horizon line for 10 deg pitch or level with the tallest of the three vertical lines for 13 deg pitch (no more than 13 deg or risk tail strike).
8. After takeoff, fly straight and climb until HUD automatically changes from takeoff to nav mode (at Mach 0.35), and waypoint automatically changes from LS to B1.

Autothrottle (AFK) -- Lever next to landing gear, behind left elbow (Pinky Button)
- Gear up (Mode 1): AFK maintains speed of 550 kph.
- Gear down (Mode 2): AFK maintains 12 deg AOA for landing.
- Gear down and Mode 3 button lit (Mode 3): AFK maintains 15.5 deg AOA for shortest possible landing.
  - Mode 3 button is on upper left instrument panel, under autopilot lights. Only use when very lightly loaded (< 40% fuel).
- Autothrottle disengages when any of these happen:
  - AFK button (Pinky Button) is pressed
  - Uncage button (Rear Thumb Button) is pressed
  - Afterburner engaged
  - Weight on nosewheel