1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Landing, After landing

Landing -- Visual approach
1. Set QFE on altimeter to value shown in kneeboard for landing waypoint.
2. Set AKT POS, OUT, press L/MAL waypoint button to select landing waypoint (L1 or L2)
3. Verify correct landing runway in nav system (if using road base, you must set this manually):
  1. Data Selector knob ... BANA GRÄNS, OUT (Runway Heading)
  2. First 4 digits are runway heading in NNN.N format, last 2 digits are ILS channel (if available).
  3. To toggle to the reciprocal runway, press L/MAL.
  4. To set custom heading:
    1. Data Selector knob ... BANA GRÄNS, IN
    2. Enter runway heading as 4-digit number, NNN.N deg and "00" at the end.
    3. Press LS/SKU, then set AKT POS, OUT.
4. Master Mode knob ... LANDNING P/O for visual approach
5. Thrust reverser ... Arm (lever in cockpit will pull out) (Front Thumb Button)
6. Gear down under 600 kph.
7. Minimum speed 260 kph.
8. Put the glide path line in the HUD on the end of the runway.
9. Put velocity vector on glide path line to get 12 degrees AOA and 3 degree glide slope.
10. Can use autothrottle (Pinky Button) to maintain 12 deg AOA.
11. When front wheel touches down, thrust reverser will engage. Use full throttle to slow down quickly (afterburner will not light).
  - Heavy braking may cause skidding.
1. Reduce throttle before coming to a complete stop and use brakes for final stop.
2. DO NOT USE BRAKES WHILE MOVING BACKWARDS.
3. See after landing instructions below.

Landing -- Instrument approach -- WIP
1. Set QFE on altimeter to value shown in kneeboard for landing waypoint.
2. Set AKT POS, OUT, press L/MAL waypoint button to select landing waypoint (L1)
3. Verify correct landing runway in nav system (if using road base, you must set this manually):
  1. LS (landing at same runway you took off from), or L1 or L2 (landing at alternate bases) waypoint must be selected.
  2. Data Selector knob ... BANA GRÄNS, OUT (Runway Heading)
  3. First 4 digits are runway heading in NNN.N format, last 2 digits are ILS channel (if available).
  4. To toggle to the reciprocal runway, press LS/SKU if using LS, or L/MAL if using L1 or L2.
  5. To set custom heading:
    1. Data Selector knob ... BANA GRÄNS, IN
    2. Enter runway heading as 4-digit number, NNN.N deg and "00" at the end.
    3. Press LS/SKU, then set AKT POS, OUT.
4. Master Mode knob ... LANDNING NAV for instrument approach
  - Waypoint will automatically be changed to LBS, LB1, or LB2, which is the approach waypoint 20 km out from the runway.
  - Radar screen will show approach waypoint (circle) and extended runway centerline.
1. Taxi and landing light switches ... As needed (underneath left front canopy rail, outboard of thrust reverser handle)
2. Thrust reverser ... Arm (lever in cockpit will pull out) (Front Thumb Button)
3. Gear down under 600 kph.
4. Minimum speed 260 kph.
5. When you reach the approach waypoint, it will change to LFS, LF1, or LF2, which is the actual touchdown point on the end of the runway.
6. Put the glide path line in the HUD on the end of the runway.
7. Put velocity vector on glide path line to get 12 degrees AOA and 3 degree glide slope.
8. Can use autothrottle (Pinky Button) to maintain 12 deg AOA.
9. When front wheel touches down, thrust reverser will engage. Use full throttle to slow down quickly (afterburner will not light).
  - Heavy braking may cause skidding.
1. Reduce throttle before coming to a complete stop and use brakes for final stop.
2. DO NOT USE BRAKES WHILE MOVING BACKWARDS.
3. See after landing instructions below.

After landing
1. Master Mode knob ... BER to reset nav computer and compile and write ELINT data
2. Remove and reinsert data cartridge, and reload waypoints, even if you're using the same flight plan. This fully resets the nav system for the next flight.