1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Navigation, Waypoints

Notes
- Terrain following system accuracy can be checked in AKT POS, OUT, the 5th digit is the status:
  - 0 = TERNAV inoperable
  - 1 = TERNAV OK, but not in use. Stand-by mode, aircraft is on ground or is outside TERNAV area.
  - 2 = TERNAV OK, rough search, attempting to find area
  - 3 = TERNAV OK, fine search, still trying to find exact location
  - 4 = TERNAV OK and tracking, but not being used. SPA master mode may show this.
  - 5 = TERNAV OK and tracking, location known and navigation system in use.
  - The 6th digit shows position error in km.
- When showing lat/longs, the latitude number has the first digit flashing, the longitude number is solid.

Add waypoints from F10 map markers
1. Add map markers with text label as shown below.
2. Remove and reinsert the data cartridge (behind left elbow).
3. Data selector knob ... REF LOLA, IN
4. Enter 9099, then press LS/SKU
5. Wait for numbers to stop flashing (about 7 seconds).
6. Data selector knob ... AKT POS, OUT
F10 map waypoint marker types
  - Bn	Nav waypoints.
  - Mn	Target waypoints.
- B and M numbers should be sequential (1-9) through all the B and M markers.
  - Un	Popup point (optional). The n is the number of the waypoint that the popup point is for.
  - BXn	Reference point. The n is independent of the Bn/Mn numbers. BX6-9 are used for RB 15 antiship missiles. See RB 15F ASM weapon page for more details.
  - LS	Starting position (your current position will be used automatically when loading the cartridge, no need to make a F10 marker for this).
  - L1	Landing waypoint (defaults to same as LS).
  - L2	Alternate landing waypoint (optional).
  - e.g. Typical flight plan might be LS -> B1 -> B2 -> M3 (with optional U3 popup point) -> M4 -> B5 (optional -> L1 (with optional L2 alternate landing))

Select a waypoint for navigation
Press the waypoint button on the right console.
  - To select landing waypoints, press L/MAL button to toggle between L1 and L2.
  - To select BXn waypoints (used for ASMs and other reference), press BX button, then corresponding Bn (1 to 9).
1. Current waypoint is shown on the right instrument panel.
2. Distance to waypoint is shown on right instrument panel dial. "Mil" = 10 km, dial will switch to "km" when under 40 km.

Add/edit a waypoint
1. Data selector knob ... REF LOLA, IN
2. Enter coordinates in DDMMSSDDMMSS format, Easting (lat) first, then Northing (long), then press the waypoint button you want to save the coordinates to, wait for display to show zeros.
  - You can also set an airport as a waypoint (Bn or LS/L1) by entering 90XX where XX is the airport code. See built-in kneeboard page for airport code numbers.
  - To set an airport as L2, enter 99XX and press L/MAL.
Data selector knob ... AKT POS, OUT
  - Waypoint location can be viewed for any waypoint with REF LOLA, OUT.

To change a nav waypoint (Bn) into a target waypoint (Mn) or vice versa
1. Data selector knob ... TAKT, IN
2. To change a nav waypoint (Bn) into a target waypoint (Mn), enter 9.
3. Or to change a target waypoint (Mn) into a nav waypoint (Bn), enter 0.
4. Then press the button of the waypoint you want to change. Change happens immediately.
5. Data selector knob ... AKT POS, OUT