1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Nav Fixes

Notes
- Terrain following system accuracy can be checked in AKT POS, OUT, the 5th digit is the status:
  - 0 = TERNAV inoperable
  - 1 = TERNAV OK, but not in use. Stand-by mode, aircraft is on ground or is outside TERNAV area.
  - 2 = TERNAV OK, rough search, attempting to find area
  - 3 = TERNAV OK, fine search, still trying to find exact location
  - 4 = TERNAV OK and tracking, but not being used. SPA master mode may show this.
  - 5 = TERNAV OK and tracking, location known and navigation system in use.
  - The 6th digit shows position error in km.
- When showing lat/longs, the latitude number has the first digit flashing, the longitude number is solid.

Nav fixes/updates
Select the waypoint you want to update.
  - Updating a Bn navigation waypoint will update all the other waypoints, including target waypoints.
  - Updating a Mn target waypoint will update only that waypoint.
  - Updating the BX8 marker waypoint will update BX6, BX7, and BX9 as well, but updating BX6, BX7, or BX9 will only update that specific waypoint.
When updating a waypoint (E or flashing E), automatic waypoint incrementing when flying over the waypoint is inhibited.
Visual f‌ly-over f‌ix
1. Radar must be Off.
2. Destination Indicator should show the waypoint you want to correct, and that you're going to fly over the actual location of.
3. Press T1 detent (shift-Ministick press) on radar stick. Destination Indicator should show a solid E.
4. When you are directly over the actual location of the waypoint, press the TV detent (Ministick press) on radar stick.
5. Waypoint location will be updated and next waypoint will be selected.
Radar f‌ix
1. Radar must be On in A1 mode (PPI display).
2. Destination Indicator should show the waypoint you want to correct, and that you're going to select the exact location of on the radar.
3. Current location of waypoint will show as a circle on the radar screen.
4. Press T1 detent (shift-Ministick press) on radar stick. Destination Indicator should show a flashing E, and a cross will appear on the radar screen.
5. Use the radar control stick (ministick on throttle) to move the cross on the radar screen to the waypoint's correct location.
6. Press the TV detent (Ministick press) on radar stick.
7. Waypoint location will be updated.