1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

305 - Flight - Radios, Jettison

Radio setup and tuning
COM1	FR22	VHF/UHF	103 to 155.975 MHz / 225.00 to 399.95 MHz	AM/FM	Main radio
COM2	FR24	VHF	Preset channels only	AM	Backup radio

Select radio with FR22 Mode Selector knob (left console behind throttle)
  1. NORM+LARM = Transmit/receive on FR22 radio, receive Guard on FR24 radio.
  2. NORM = Transmit/receive on FR22 radio only.
  3. LARM, E, F, or G = Transmit/receive on FR24 radio only, on preset channels (see built-in kneeboard page). LARM is channel H (Guard, 121.000 MHz).
FR22 Preset radio channels
Built-in kneeboard pages list Airbases, Radio Channels, and Groups:
Airbases (lists airbases on the map):
Set the right-hand knob to the airbase number, then press the letter button on the second row for the corresponding frequency from the kneeboard.
Radio Channels (regular common channels):
1. Special 1, Special 2, Special 3, and H are the forward-most row of buttons (H is normally Guard, "‒" button is manual frequency, see below)
2. E, F, G are the backup FR24 radio channels.
Groups ("X-Y" format):
Set the left-hand knob to the first ("X") number, then press the button for the second ("Y") number on the rearward rows of numbers.
FR22 Manual frequency tuning
1. Set FR22 Mode Selector knob to NORM+LARM or NORM.
2. Press "‒" channel button (forward right).
3. Set frequency and AM/FM on manual frequency panel (left instrument panel bottom).
FR24 Preset radio channels (only preset channels can be used with FR24, no manual tuning)
Set FR22 Mode Selector knob (left console behind throttle) to LARM, E, F, or G. See built-in kneeboard pages for preset channel frequencies. LARM is channel H (Guard, 121.000 MHz).

Jettison
- External fuel tank: External Fuel Tank Release button (covered switch, right wall forward) (T3 switch to open, T2 switch to push jettison button)
- External stores (except outboard Sidewinders and countermeasure/ECM pods): Weapon Emergency Release button (covered switch, right wall forward)