1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Bombs, Rockets, Guns

Mixed weapon loadouts
Mixed loadouts are not valid, except the following: RB-24/-24J A2A missiles are allowed with any loadout, and AKAN 30 mm gunpods are allowed with RB-75 (Maverick) or RB-05A (MCLOS) missiles.

				QFE reqd?	waypoint reqd?	radar ranging?
Level (CCRP)	PLAN	ANF	LD/HD	no	no	yes
Direct	PLAN	NAV	LD only	no
CCIP	PLAN	NAV	HD only	yes?

Precision	DYK	ANF
Quick	DYK	NAV

Radar release	RR	ANF
Nav/Toss release	RR	NAV

M/71 High-drag bombs (with parachute and nose probe) -- 120 kg (265 lb) GP bombs, 4 per pylon
"Level" release -- Level bombing with CCRP
  1. Weapon Selector dial ... SJO PLAN (default)
  2. Interval dial ... 10 to 60 as needed (distance in m)
  3. Release Mode switch ... SERIE (default)
  4. Set QFE on altimeter to value shown in kneeboard for target waypoint (only required for steering cues, not for bomb accuracy)
  5. When approaching target waypoint (Mx): Master Mode dial ... ANF
  6. Speed 0.7 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
  7. Put dot on HUD on the actual target location (ideally should be inside the target indicator circle), then hold trigger UNSAFE (Trigger 1st stage) to designate the target location.
  8. HUD symbology will "jump" and now the dot gives steering directions to release point. Keep the dot inside the circle.
  9. 2 seconds before release, range bar at bottom will start flashing. Press and hold Trigger 2nd stage to give release consent.
  10. At release point, dot will show "wings". Keep trigger held until all bombs are gone.
  - You can use this mode against targets of opportunity, even with invalid QFE setting. The circle steering cue will be missing or inaccurate, but if you keep flying straight after designating the target with Trigger UNSAFE, the bomb drop should be fairly accurate.
"CCIP" release -- Low altitude bombing with CCIP (high-drag bombs only)
  1. Weapon Selector dial ... SJO PLAN (default)
  2. Interval dial ... 10 to 60 as needed (distance in m)
  3. Release Mode switch ... SERIE (default)
  4. Master Mode dial ... NAV
  5. Set QFE on altimeter to value shown in kneeboard for target waypoint (required for CCIP accuracy).
  6. Hold trigger UNSAFE (Trigger 1st stage) to show HUD CCIP symbology.
  7. Bombs will fall between dot and circle.
    - If dot and circle don't appear, you may be too high and/or slow.
  1. Speed 0.7 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
  2. Release height 50 m to 200 m.
  3. Hold Trigger 2nd stage to drop until all bombs are gone.
Dive bombing with CCIP -- DYK mode
  1. Weapon Selector dial ... MARK DYK
  2. Interval dial ... as needed (distance in m)
  3. Release Mode switch ... SERIE (default)
  4. Master Mode dial ... ANF to use radar ranging, or NAV to use triangulation ranging
  5. QFE setting only required in order to have an accurate target indicator circle (shows where the target is on the ground).
  6. When near the target, pop up and dive on the target. Put the center dot in the HUD on the target's actual location and hold trigger UNSAFE (Trigger 1st stage) to begin radar ranging. A "fin" will appear over the dot to indicate radar ranging is active.
  7. Hold the dot on the target. 2 seconds before release, range bar at bottom of HUD will begin flashing. When dot shows "wings", hold Trigger 2nd stage to drop until all bombs are gone.
- Any altitude level bombing with CCRP -- RR mode
  - Target at waypoint -- NAV mode
  - Target designated on radar -- ANF mode

M/71 Low-drag bombs (no parachute or nose probe) -- 120 kg (265 lb) GP bombs, 4 per pylon
- PLAN mode (CCRP level bombing)
  - Min height: Approx 200m AGL. Bombs can be safely dropped as low as 150 m without damage, but won't be accurate.
  1. Weapon Selector dial ... SJO PLAN (default)
  2. Interval dial ... as needed (distance in m)
  3. Release Mode switch ... SERIE (default)
  4. Master Mode dial ... NAV
  5. Set QFE on altimeter to value shown in kneeboard for target waypoint.
  6. Hold trigger UNSAFE (Trigger 1st stage) to show HUD symbology.
  7. Bombs will fall between dot and circle.
  8. Speed 0.7 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
  9. Release height 50 m to 200 m.
  10. Hold Trigger 2nd stage to drop until all bombs are gone.
DYK mode (CCIP dive bombing) -- low-drag or high-drag
  1. Weapon Selector dial ... SJO DYK
  2. Interval dial ... as needed (distance in m)
  3. Release Mode switch ... SERIE (default)
  4. Master Mode dial ... NAV
  5. Set QFE on altimeter to value shown in kneeboard for target waypoint.
  6. Hold trigger UNSAFE (Trigger 1st stage) to show HUD symbology.
  7. Bombs will fall between dot and circle.
  8. Speed 0.7 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
  9. Release height 50 m to 200 m.
  10. Hold Trigger 2nd stage to drop until all bombs are gone.

ARAK M/70B rockets -- 135 mm (5.3 in), 6 per pod, HE-Frag or HEAT
Short range mode (1 km to 3 km)
1. Weapon Selector dial ... ATTACK
2. Release Mode switch: NORM/SERIE (up, default) for Short Range
3. Second Release Mode switch switch:
  1. GRUPP/VALB (up) for all rockets per pod (press trigger once fires all rockets in 0.6 sec).
  2. ENKEL/STD (down) for single rocket per pod per trigger press
4. When approaching target waypoint, Master Mode dial:
  1. ANF for automatic continuous target ranging
  2. NAV for manual target ranging (hold Trigger Unsafe to range)
5. (optional) Set QFE on altimeter to value shown in kneeboard for target waypoint. (Not required, only affects the placement of the target indicator ring, not the rocket accuracy.)
6. Pop up and dive on the target. Must be diving more than 5 deg for radar ranging to work.
7. Put small solid center dot on the target. Hollow ring should show location of target.
8. Hold Trigger Unsafe to begin radar ranging (if in NAV mode). Target indicator ring will disappear.
9. Distance line at bottom flashes when within 2 seconds of release.
10. When in range, "wings" appear to either side of center dot. Press and hold trigger to fire.
Long range mode (6 km to 7 km)
1. Weapon Selector dial ... ATTACK
2. Release Mode switch: LA/IMP (down) for Long Range
3. Second Release Mode switch switch:
  1. GRUPP/VALB (up) for all rockets per pod (press trigger once fires all rockets in 0.6 sec). Recommended for long range mode.
  2. ENKEL/STD (down) for single rocket per pod per trigger press
4. When approaching target waypoint, Master Mode dial:
  1. ANF for automatic continuous target ranging
  2. (Cannot be in NAV mode for long range rockets)
5. (optional) Set QFE on altimeter to value shown in kneeboard for target waypoint. (Not required, only affects the placement of the target indicator ring, not the rocket accuracy.)
6. Pop up and dive on the target. Must be diving more than 3 deg for radar ranging to work.
7. Put small solid center dot on the target. Hollow ring should show location of target.
8. Hold Trigger Unsafe. Target indicator ring will disappear??
9. Distance line at bottom flashes when within 2 seconds of release.
10. When in range, "wings" appear to either side of center dot. Press and hold trigger to fire.

AKAN 30/55 gun pods -- 30 mm, 150 rounds per pod
1. Weapon Selector dial ... ATTACK
2. Release Mode switch ... SERIE (default)
3. When approaching target waypoint, Master Mode dial ... ANF
4. Set QFE on altimeter to value shown in kneeboard for target waypoint. (Not strictly required?? Seems to only affect the placement of the target indicator ring, not the rocket accuracy.)
5. Pop up and dive on the target. Must be diving more than 5 deg for radar ranging to work.
6. Put center dot on the target. Target indicator ring should show location of target.
7. Hold Trigger Unsafe to begin radar ranging. Target indicator ring will disappear.
8. Distance line at bottom flashes when within 2 seconds of release.
9. When in range, "wings" appear to either side of center dot. Press and hold trigger to fire.