1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - BK 90 glide cluster bombs

Mixed weapon loadouts
Mixed loadouts are not valid, except the following: RB-24/-24J A2A missiles are allowed with any loadout, and AKAN 30 mm gunpods are allowed with RB-75 (Maverick) or RB-05A (MCLOS) missiles.

BK 90 Mjolnir glide cluster bomb -- MJ1 is 72x HE/frag bomblets, MJ2 is 24x AP bomblets
1. Weapon Selector dial ... ATTACK
2. Release Mode switch ... SERIE (default)
3. Set QFE on altimeter to value shown in kneeboard for target waypoint.
4. Default bomb approach altitude is 60 m AGL (internal radar altimeter). To change:
  1. Set Targeting Mode switch to VALB (default). (If set to STD, height will be 60 m.)
  2. Set TAKT - IN.
  3. Enter 91, then three digit altitude in m (30 to 500 m).
     910300 = 30 m, 915000 = 500 m. Default is 60 m (or 910000).
  4. Press LS, then set AKT POS - OUT.
5. Default bomb pattern is Compact, both bombs burst over same location. Bomb patterns only work if dropping both bombs in SERIE. To change:
  1. Set TAKT - IN, then enter:
    - 921000 for Long (bombs burst in line one after the other)
    - 922000 for Wide (bombs burst next to each other)
    - 923000 or 920000 for Compact (default)
  1. Press LS, then set AKT POS - OUT.
2. When approaching target waypoint, set Master Mode dial to ANF.
3. Speed 0.6 to 0.9 Mach. Use Stage 2 AB for about 0.85 Mach.
4. Height 50 m to 500 m.
5. Hold trigger UNSAFE to show HUD symbology.
6. Starting about 10 km away, distance bars will appear at bottom of HUD. When horizontal line is within the outer vertical bars, target is in range. Max range is about 6 to 7 km at 0.9 Mach
7. Press and hold trigger to release. First bomb will release about 1.3 seconds after trigger is held, second one will be 1.5 sec later. You must press the trigger again to drop the second pair if you're carrying 4.
Pattern of HE/FRAG warheads is approx 300m long (in direction of travel) and 120-150m wide.