1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing

Takeoff
1. Elevator Trim ... -1.5 deg (indicator on upper left instrument panel, down 1.5 lines)
2. Flaps ... TAKE OFF (middle switch position)
3. Engine Ignition Switch ... CONT IGN (aft position) (just in front of throttle)
4. MPR power ... Engage (Front Thumb Button) (light on upper right instrument panel will go on)
5. Brakes will hold full mil and MPR power.
6. Begin takeoff run. Use differential brakes up to 40 kts, rudder after that.
7. Rotate at approx 110-130 kts, heavier is faster.
8. Put horizon level with the top of the gunsight base for good angle.
9. Retract gear before 200 kts.
10. Retract flaps before 190 kts.
11. Engine Ignition Switch ... OFF (middle position)

Landing
Landing gear warning horn sounds when under 75% N1 (slightly over 50% physical throttle) and gear is not down. Cannot be canceled (I think??) but volume can be adjusted with INT knob on AUDIO panel.
1. Engine Ignition Switch ... CONT IGN (aft position) (just in front of throttle)
2. Speedbrakes ... Out full, and keep out through landing
3. Under 200 kts: Landing gear ... Down
4. Under 190 kts: Flaps ... TAKE OFF (middle switch position)
5. Under 150 kts: Flaps ... DOWN FULL (bottom switch position)
6. Slow to On Speed AOA (approx 120 kts, top light=too slow, bottom light=too fast) and trim.
  - Will probably require full nose-up trim.
1. Adjust pitch with throttle.
2. Aim at end of runway. Approach angle/glideslope should be 3°.
3. Cut throttle at runway threshold, flare at 110 kts, touchdown at 95 kts, aerobrake until nose drops.
4. After stopping, retract airbrake, set flaps to up, and Engine Ignition Switch ... OFF (middle position).

ILS precision landing
1. On VHF-NAV panel (right console):
  1. Mode knob ... NAV
  2. Tune ILS frequency on NAV frequency dials (right knob and readout)
2. Verify NAV button is lit (right-most of 3 buttons to left of HSI), which means it's using the receivers in your cockpit and not the other one.
3. Set HSI to NAV (button on right side of HSI, toggles ADF/NAV)
4. Set runway heading as course on HSI (Middle Finger Hat up/down or course knob on HSI panel on right console rear)
5. When red "LOC" flag at bottom of HSI disappears, ILS info is being received. Press the APR button on the Flight Director panel (above right knee). HDG and NAV buttons should also light up automatically with "CAP" lights indicating ILS signals have been captured.
6. HSI needles show the localizer (horizontal) and glideslope (vertical). Fly the needles to the end of the runway.