1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

101 - Controls - Joystick
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger
- P1: --
- P2: Toggle Red or Yellow Smoke Colorant when smoke system is on
Flip-down Trigger -- Trigger safety (Red or Yellow Smoke system)
- P: Trigger safety off
- S-P: Trigger safety on
Red Button
- P: White Smoke system toggle on/off
- S-P (3x): Eject
Upper Gray Button
P: Center VR view
Lower Gray Button
P: --
Trim Hat
U/D/L/R: Pitch/Roll Trim
Dish Hat -- Weapon release safety (white smoke system)
- U: Weapon release safety off
- D: Weapon release safety on
MANVR/PC hat -- Mouse and zoom
Index Finger Hat -- View and Game controls
- F: F6 Weapon view	S-F: Active pause
- B: F2 External view	S-B: Info bar view toggle
- U: F1 Cockpit view	S-U: Rearm/Refuel window
- D: F10 Map view	S-D: Show controls indicator
- P: Toggle show control stick	S-P: Toggle show pilot body
Gray Reset Hat
- F: --
- B: --
- R: --
- L: --
- P: Stick Go Around button (C-101CC only)
Brake lever
P: --