1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Cold Start

Cold Start Checklist -- (default auto start sequence is about 3:45)
1. Parking Brake ... On (pulled out) (left front wall)
2. Throttle ... Fully aft
3. Ground crew ... External Power ON (backslash, F8, F2, F1)
  - GPU button (left console forward) should show "GPU" lit.
1. Oxygen Valve switch ... O (forward) (right console middle, outboard)
2. BATTERIES switch ... ON (right front wall bottom)
3. MASTER WARNING and MASTER CAUTION ... Reset (press lights on top left and right instrument panel)
4. GPU button ... Press to activate ground power (left console forward), button will show "GPU" and "ON" lit (left console forward)
  - Wheel chocks will automatically be removed when GPU is enabled.
1. BUS TIE switch ... ON (right front wall bottom)
2. MASTER WARNING and MASTER CAUTION ... Reset (press lights on top left and right instrument panel)
3. INVERTER switch ... NORMAL (up) (right front wall)
4. On FUEL panel (left console front):
  1. Fuel Transfer Pump switches ... AUTO (forward) for all tanks with fuel (green lights), OFF (middle) for any tanks without fuel (red lights)
  2. FUSELAGE TANK PUMP button ... ON; "OFF" light will turn off (transparent guarded switch)
  3. FUEL SWITCH button ... ON; "OFF" light will turn off (transparent guarded switch)
5. IGNITION switch ... START for 2 seconds, then release (left console in front of throttle)
6. When N2 gauge reaches 10%: Throttle ... IDLE (Bottom Thumb Button press)
  - Engine should stabilize at: N1 29-33%, ITT approx 520 deg C, N2 58-71%, fuel flow approx 230 lbs/hr.
1. GPU button ... Press to deactivate ground power (left console forward), button will show only "GPU" lit (left console forward)
2. Ground crew ... External Power OFF (backslash, F8, F2, F2)
  - GPU button (left console forward) should show nothing lit.
1. GENERATOR switch ... RESET (left click), then ON (right click) (right front wall)
2. Standby Artificial Horizon ... Uncage and align with horizon (right instrument panel)
3. IFF MASTER knob ... NORM (center console between legs)
4. IFF MODE 4 switch ... ON (center console between legs)
5. Canopy ... Close and lock (T7 switch up or down, once to close, again to lock)
6. Wait for AHRS to synchronize: Backup compass (right canopy bow), HSI compass, and RMI compass (left of HSI) should all be the same.
7. Parking Brake ... Release (pushed in) (left front wall)

Proceed with rest of preflight checklist on next page.